## Slide 1: Lecture 7-2 Design For Area Minimization
Tian Sheuan Chang

## Slide 2: Outlines
Analysis of area cost
Algorithm: Complexity reduction
Architecture: resource sharing

## Slide 3: Analysis of Area costs

## Slide 4: Synthesis
Synthesis = Translation + Logic Optimization + Technology Mapping
always @ (a, b)
case ({a,b})
2’b00: out = 1; 2’b01: out = 1; 2’b11: out = 1; default: out = 0;
endcase
out  ab  ab  ab
Translation
Logic
Optimization
out  a b
a b
Out
Technology Mapping
0
1
0
1
Out
0
1
b
1
1
0
1
a
2-input LUT
ASIC
FPGA

## Slide 5: Synthesis is Constraint-Driven
(Delay)
(Area)
(Power Consumption)
Area
Large
Small
Delay
Long
Short
You should specify your constraints
Synthesizer optimizes the design to meet the constraints
Synthesis Constraint

## Slide 6: HDL for Synthesis
“Bad” HDL code does not allow efficient optimization during synthesis
  Garbage in, garbage out!
Logic synthesizer doesn’t do magic! designer has to take some responsibility in coding.
Example:
input sub; input [3:0] a,b;
output [3:0] y;
assign y = sub ? (a-b) : (a+b)
input sub; input [3:0] a,b;
output [3:0] y;
wire [3:0] tmp;
assign tmp = sub ? ~b : b; assign y = a + tmp + {3’b0,sub}
b[3:0]
a[3:0]
sub
0
1
Y[3:0]
4
4
b[3:0]
a[3:0]
sub
0
Y[3:0]
4
4 1
Ci
Y[3:0]
More efficient

## Slide 7: HDL for Synthesis (General Guidelines)
Think Hardware:
  Write HDL hardware descriptions
    Think of the topology implied by the code
  Do not write HDL simulation models
    No explicit delays
    No file I/O
Think RTL:
  Writing in an RTL coding style means describing:
    Register architecture
    Circuit topology
    Functionality between registers
  Synthesis tool optimizes logic between registers:
    It does not optimize the register placement

## Slide 8: How to Read You Area Reports
****************************************
Report : area
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Library(s) Used:
XXXXX
Number of ports: 5
Number of nets: 9
Number of cells: 5
Number of references: 4
Combinational area: 7.000000
Noncombinational area: 0.000000
Net Interconnect area: undefined (Wire load has zero net area)
Total cell area: 7.000000
Total area: undefined
****************************************
Report : timing
-path full
-delay max
-max_paths 1
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Operating Conditions:
Wire Load Model Mode: enclosed
Startpoint: in[2] (input port)
Endpoint: isprime (output port)
Path Group: (none)
Path Type: max
Des/Clust/Port Wire Load Model Library
------------------------------------------------
prime 2K_5LM XXXXX
Point Incr Path
-----------------------------------------------------------
input external delay 0.000 0.000 r
in[2] (in) 0.000 0.000 r
U4/Y (EX210) 0.191 0.191 f
U5/Y (BF051) 0.116 0.307 r
U1/Y (BF052) 0.168 0.475 f
isprime (out) 0.000 0.475 f
data arrival time 0.475
-----------------------------------------------------------
(Path is unconstrained)
Left part: area report
Right part: timing report
Noncombinational part: DFF, SRAM, latch

## Slide 9: Area Estimation
1 DFF, 1 adder, 1 2:1 MUX:
  7 gate counts
  1 gate count == NAND2x1 area
Multiplier: depends on architecture
  NxN => N^2 * 7
Estimate data flow part first
  How many adder/multiplier have been used
Control part (FSM)
  Extra 5 to 10% area cost

## Slide 10: Where your area goes?
Use Synopsys Design Compiler to analyze this
  Not covered in this course
Code review
  Sequential part: Count DFF numbers generated in each always_ff
    Unique output variables in the Verilog commands
    Avoid unnecessary pipeline or DFF storages
  Data path part
    Count adder/multiplier and other and/or logic
  Controller part
    Simplify your FSM
Rule of thumb
  Controller: take 5 to 10% of area
  Data path takes 40% to 70%, memory or buffers takes the rest

## Slide 11: Complexity Reduction
Easy to do
  Remove constant operations or
  Simplify operations
  Find common terms/regularity/shared data in the algorithms (e.g. share DFF in parallel FIR filter, or complex if-else conditions)
Algorithm optimization
  Application dependent
  Something more like used in C program
  E.g. assign y = a * b;
  If b = 4’h2;
    assign y = a << 1;

## Slide 12: Area optimization

## Slide 13: Concept
Folding (or rolling up the pipeline)
  Time sharing the same logic to save area
Algorithm change

## Slide 14: Area-related Techniques:
Area is the second primary factors of a digital design
  A topology that targets area is one that reuses the logic resources to the greatest extent possible, often at the expense of throughput (speed).
  This requires a recursive data flow, where the output of one stage is fed back to the input for similar processing.

## Slide 15: Area-related Techniques: Rolling Up the Pipeline
Opposite to the unrolling the loop to increase throughput
  Unrolling the loop achieved by adding more registers to hold intermediate values, i.e., more area
  Thus to reduce the area the reversed action should be done (i.e., Sharing)
Resource Sharing is used where there are functional blocks that can be used in other areas of the design or even in different modules
  Sharing logic resources requires special control circuitry to determine which elements are input to the particular structure

## Slide 16: Rolling Up the Pipeline
Calculation of P = A*B
  A: a normal integer with the fixed point just to the right of the LSB (8 bits)
  B: a fractional number with a fixed point just to the left of the MSB (8 bits)
  P: the product, which requires only 8-bits
One implementation alternative:
  Critical path: one multiplier (complex itself)
  One product every clock cycle (high throughput)
module mult8(
output [7:0] P,
input [7:0] A,
input [7:0] B, input clk);
reg [15:0] prod16; assign P= prod16[15:8]; always @(posedge clk) prod16 <= A * B; endmodule

## Slide 17: Rolling Up the Pipeline : Resource Sharing
Rolling Up the Pipeline:
  Using series of shift-and-add operations
  Smaller critical path
  Less area due to the simple operations and sharing
  One product every 8 clock cycles! (low throughput)
module mult8(output done,output reg [7:0] product, input [7:0] A, input [7:0] B, input clk, input start);
reg [4:0] multcounter; // number of shift/adds reg [7:0] shiftB; // shift register for B
reg [7:0] shiftA; // shift register for A wire adden; // enable addition assign adden = shiftB[7] & !done; assign done = multcounter[3]; always @(posedge clk) begin if(start) multcounter <= 0;
else if(!done) multcounter <= multcounter + 1;
// shift register for B if(start) shiftB <= B;
else shiftB[7:0] <= {shiftB[6:0], 1’b0};
// shift register for A
if(start) shiftA <= A;
else shiftA[7:0] <= {shiftA[7], shiftA[7:1]};
// calculate multiplication if(start) product <= 0;
else if(adden) product <= product + shiftA;
end
endmodule

## Slide 18: Resource Sharing: Area Reduction Technique
Back to FIR Filter:
  Three multiplications, two adders, two registers
X(n)
a
b
Y(n)
Y(n) = ax(n) + bx(n-1) + cx(n-2)
X(n-1)
X(n-2)
c

## Slide 19: Resource Sharing: Area Reduction Technique
Sharing the Multiply-Accumulate (MAC) to reduce area:
  One multiplication, one adder, one register
  Requires some control logic to determine which input is inserted (FSM)
DataIn
Coeff
MAC
DataIn=X[0], 0,0,0, X[1], 0,0,0,X[2], ….
Coeff= a, b, c, 0,a, b, c, 0, ...
Out
DataIn
Coeff
multcoeff
multdat
multout
accumsum
accum
State == 0
0
1
16'b0
State
X0
X1
X2
State == 0
0
1
16'b0

## Slide 20: Resource Sharing: Area Reduction Technique
module sharing( output reg [15:0] Out, input clk,
input [7:0] datain, // X[0]
input [7:0] coeffA, coeffB, coeffC); // coeffs for low pass filter
// define input/output samples
reg [7:0] X0, X1, X2;
reg [2:0] state; // holds state for sequencing through mults wire [15:0] accum; // accumulates multiplier products
reg [15:0] accumsum;
wire [15:0] multout; // multiplier product reg [7:0] multdat;
reg [7:0] multcoeff;
assign multout =(state==0)?16'b0:multcoeff * multdat;
// clearing and loading accumulator
assign accum = (state==0)?16'b0:accumsum;
always @(posedge clk)
accumsum <= accum + multout;
always @ (posedge clk) begin
case(state)
0: begin // load new data
X0 <= datain; X1 <= X0; X2 <= X1;
multdat <= datain; multcoeff <= coeffA; state <= 1;
Out <= accumsum;
end
1: begin // A*X[0] is done, load B*X[1] multdat <= X1; multcoeff <= coeffB; state <= 2;
end
2: begin // B*X[1] is done, load C*X[2] multdat <= X2; multcoeff <= coeffC; state <= 3;
end
3: begin // C*X[2] is done, load output state <= 0;
end default
state <= 0;
endcase end endmodule

## Slide 21: Resource Sharing: Area Reduction Technique

## Slide 22: Resource Sharing: Area Reduction Technique
HDL coding style can force a specific topology to be synthesized
A B C
A
B
D A
B
E
SUM1
SUM2
SUM3
A
B C
D
E
SUM1
SUM2
SUM3
Sharing
SUM1 = A+B+C; SUM2 = A+B+D; SUM3 = A+B+E;
assign tmp = A+B; SUM1 = tmp +C; SUM2 = tmp +D; SUM3 = tmp +E;

## Slide 23: Resource Sharing: Area Reduction Technique
Let’s assume we have two counters controlling different design sections
  CounterA, a free running 8-bit counter
  CounterB, an 11-bit counter, counting from 0 to 1666 and resets to zero

## Slide 24: Resource Sharing: Area Reduction Technique
Resource-shared version of these two counters
For compact designs where area is the primary requirement, search for resources that have similar counterparts in other modules that can be brought to a global point in the hierarchy and shared between multiple functional areas.
Shared Part

## Slide 25: Architectural Techniques : Resource Sharing

## Slide 26: Resource sharing
assign y = a == 1 ? b * c : e * f;
t1 = a == 1 ? b : e; t2 = a == 1? c : f; y = t1 * t2;
Find the resource that can be shared
  Resource: high area cost part, like adder, multiplier
  Tool may or maynot find these opportunities