## Slide 1: Digital Circuits and Systems Lecture 9 Factoring State Machines
大的FSM要如何設計?若其中state變化有規則，可以把有規則的部分獨立
Tian Sheuan Chang

## Slide 2: Outline [Dally Ch.17]
Light flasher
Traffic light controller

## Slide 3: 大的FSM要如何設計? Design A Large FSM
先講結論 Short Summary
若其中state變化有規則，或較獨立部分
  可以把有規則的部分或較獨立部分，單獨分離開來 Separate the regular part
  形成階層式FSM, Design a hierarchical FSM
好處
  更簡單
  所需硬體更少

## Slide 4: 設計哲學: 把大問題切割成小問題，比較好作
Divide and Conquer: Divide a big problem into several smaller problems
Last lecture - data/control partitioning
This lecture – factoring state machines
Later – system partitioning
Similar to factoring in logic design and constant multiplication
a(b+c)+bc = ab+ac+bc
X*(0110110110112 )= X*011*(20 + 23 + 26 +29)

## Slide 5: Light flasher

## Slide 6: Specification Of Light Flasher
Inputs: in
Outputs: out
Operation:
  When in = 1, FSM goes through 5 sequences:
  On-Off-On-Off-On
  Each On sequence:
    out = 1
    6 cycles long
  Each Off sequence:
    out = 0
    4 cycles long
  After 5 sequences, FSM goes back to OFF state to wait for new input

## Slide 7: Light Flasher State Diagram
  On-Off-On-Off-On
  Each On sequence:
    out = 1
    6 cycles long
  Each Off sequence:
    out = 0
    4 cycles long
這很直接，但很多on 或 off
作的事情一樣，可以不用那麼多
State
Notes: 估算DFF數量和MUX cost
State registers, state logic

## Slide 8: Factored light flasher
*Timer loads value 5 or 3, based on tsel
把數on 或off cycle數量的電路獨立
以便共用

## Slide 9: State diagram of factored light flasher
  On-Off-On-Off-On
  Each On sequence:
    out = 1
    6 cycles long
  Each Off sequence:
    out = 0
    4 cycles long

## Slide 10
module Flash(clk, rst, in, out) ;
input clk, rst, in ; // in triggers start of flash sequence
output out ; // out drives LED
reg out ; // output
wire [`SWIDTH-1:0] state, next ; // current state
reg [`SWIDTH-1:0] next1 ; // next state without reset
reg tload, tsel ; // timer inputs
wire done ; // timer output
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// instantiate timer: data path
Timer1 timer(clk, rst, tload, tsel, done) ;
always @* begin
case(state)
`S_OFF: {out, tload, tsel, next1} =
{1'b0, 1'b1, 1'b1, in ? `S_A : `S_OFF } ;
`S_A: {out, tload, tsel, next1} =
{1'b1, done, 1'b0, done ? `S_B : `S_A } ;
`S_B: {out, tload, tsel, next1} =
{1'b0, done, 1'b1, done ? `S_C : `S_B } ;
`S_C: {out, tload, tsel, next1} =
{1'b1, done, 1'b0, done ? `S_D : `S_C } ;
`S_D: {out, tload, tsel, next1} =
{1'b0, done, 1'b1, done ? `S_E : `S_D } ;
`S_E: {out, tload, tsel, next1} =
{1'b1, done, 1'b1, done ? `S_OFF : `S_E } ;
default:{out, tload, tsel, next1} =
{1'b1, done, 1'b1, done ? `S_OFF : `S_E } ;
endcase
end
assign next = rst ? `S_OFF : next1 ;
endmodule

## Slide 11: Waveforms from simulation of light-flasher FSM

## Slide 12: Still redundancy in state diagram
States A, C, E are similar (Flash on)
States B, D are similar (Flash off)
Can we reduce the state number by looking into these similar features?
還可以再化簡，除原來數on/off 的cycle數外，用另一個算剩下的flash 個數
=> Double factored FSM
  On-Off-On-Off-On
  On-Off-On-Off-On

## Slide 13: Factor out “flash number”
Why factoring out? Speed and programmability.
  On-Off-On-Off-On

## Slide 14: State diagram of double-factored light flasher
Off: timer, counter load 要倒數的值 (n-1: e.g 3 for four flashes)
FLASH: out =1 (on), timer 開始倒數，counter 不數，數到最後一個cycle, tdone = 1, 看cdone值進入space 或off
SPACE: out = 0 (off), timer 開始倒數，counter 不數，數到最後一個cycle, tdone = 1, counter-1 ，進入FLASH
  On-Off-On-Off-On

## Slide 15
module Flash2(clk, rst, in, out) ;
input clk, rst, in ; // in triggers start of flash sequence
output out ; // out drives LED
reg out ; // output
wire [`XWIDTH-1:0] state, next ; // current state
reg [`XWIDTH-1:0] next1 ; // next state without reset
reg tload, tsel, cload, cdec ; // timer and countr inputs
wire tdone, cdone ; // timer and counter outputs
// instantiate state register
DFF #(`XWIDTH) state_reg(clk, next, state) ;
// instantiate timer and counter
Timer1 timer(clk, rst, tload, tsel, tdone) ;
Counter1 counter(clk, rst, cload, cdec, cdone) ;
always @(*) begin
case(state)
`X_OFF: {out, tload, tsel, cload, cdec, next1} =
{1'b0, 1'b1, 1'b1, 1'b1, 1'b0,
in ? `X_FLASH : `X_OFF } ;
`X_FLASH:{out, tload, tsel, cload, cdec, next1} =
{1'b1, tdone, 1'b0, 1'b0, 1'b0,
tdone ? (cdone ? `X_OFF : `X_SPACE) : `X_FLASH } ;
`X_SPACE:{out, tload, tsel, cload, cdec, next1} =
{1'b0, tdone, 1'b1, 1'b0, tdone,
tdone ? `X_FLASH : `X_SPACE } ;
endcase
end
assign next = rst ? `X_OFF : next1 ;
endmodule

## Slide 16: Waveforms from simulation of twice-factored light flasher

## Slide 17: Modifying the light flasher
Making the light’s “on” state last 7 cycles
Adding 2 more “on” states
The 3rd “on” lasts 15 cycles
Making the light flash 206 times, which each flash lasting an arbitrary, predetermined number of cycles
Exercise: use the previous example to meet these
requirements by changing parameters from the datapaths.

## Slide 18: Traffic light controller

## Slide 19: Cynical view of lecture up to now
All we’ve done is build a counter with three subfields
  Each field increments when previous field “wraps”
  Most significant field is count
  Next is on/off
  Least is timer
Lets look at a less trivial problem

## Slide 20: Specification Of A New Traffic-Light Controller
Inputs: car_ew, car_lt 東西向，左轉車輛
Outputs: nsgyr ewgyr ltgyr 南北向，東西向，左轉燈號
Operation:
  Default: green light for north-south road
  If car_lt: green light for left-turn
    If ~car_lt & car_ew: green light for east-west road
  Green light for left-turn and east-west roads stay on until either:
    No more cars, or
    Green light timer expires
  Each green, yellow, and red light stay on for a time interval
  Lighting sequence: green -> yellow -> red

## Slide 21: Number of states required by ‘flat’ machine
Sequences for NS, EW, LT (3)
States in each sequence Yellow, Red, Green (3)
Time in each state 9, 5, or 4 cycles (6)
Time remaining before return to NS (13)
Total states 3 x 3 x 6 x 13 = 702
階層式看法
Sequences for NS, EW, LT (3)
  States in each sequence Yellow, Red, Green (3)
    Time in each state 9, 5, or 4 cycles (6)
Time remaining before return to NS (13)

## Slide 22: Block diagram of factored machine
Decide direction
Time to force light
back to north south
Sequences for NS, EW, LT (3)
  States in each sequence Yellow, Red, Green (3)
    Time in each state 9, 5, or 4 cycles (6)
Time remaining before return to NS (13)

## Slide 23: State diagram of master FSM
無車
紅綠燈轉換
綠燈逾時
方向燈號
綠燈時間倒數

## Slide 24
//----------------------------------------------------------------------
//Master FSM
// car_ew - car waiting on east-west road
// car_lt - car waiting in left-turn lane
// ok - signal that it is ok to request a new direction
// dir - output signaling new requested direction
//----------------------------------------------------------------------
module TLC_Master(clk, rst, car_ew, car_lt, ok, dir) ;
input clk, rst, car_ew, car_lt, ok ;
output [1:0] dir ;
wire [`MWIDTH-1:0] state, next ; // current state and next state
reg [`MWIDTH-1:0] next1 ; // next state without reset
reg tload ; // timer load
reg [1:0] dir ; // direction output
wire tdone ; // timer completion
// instantiate state register
DFF #(`MWIDTH) state_reg(clk, next, state) ;
// instantiate timer
Timer #(`TWIDTH) timer(clk, rst, tload, `T_EXP, tdone) ;
always @(state or rst or car_ew or car_lt or ok or tdone) begin
case(state)
`M_NS: {dir, tload, next1} =
{`M_NS, 1'b1, ok ? (car_lt ? `M_LT
: (car_ew ? `M_EW : `M_NS))
: `M_NS} ;
`M_EW: {dir, tload, next1} =
{`M_EW, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_EW} ;
`M_LT: {dir, tload, next1} =
{`M_LT, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_LT} ;
default: {dir, tload, next1} =
{`M_LT, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_LT} ;
endcase
end
assign next = rst ? `M_NS : next1 ;
endmodule
決定目前主要綠燈方向

## Slide 25: Block diagram of factored machine

## Slide 26: State diagram of light FSM
On signal indicates that a green light is requested.
Note. tdone here refers to the local timer signal in this light FSM

## Slide 27: Light “handshake”

## Slide 28
module TLC_Light(clk, rst, on, done, light) ;
input clk, rst, on ;
output done ;
output [2:0] light ;
reg [2:0] light ;
reg done ;
wire [`LWIDTH-1:0] state, next ; // current state, next state
reg [`LWIDTH-1:0] next1 ; // next state w/o reset
reg tload ;
reg [`TWIDTH-1:0] tin ;
wire tdone ;
// instantiate state register
DFF #(`LWIDTH) state_reg(clk, next, state) ;
// instantiate timer
Timer timer(clk, rst, tload, tin, tdone) ;
always @(state or rst or on or tdone) begin
case(state)
`L_RED: {tload, tin, light, done, next1} =
{tdone & on, `T_GREEN, `RED, !tdone,
(tdone & on) ? `L_GREEN : `L_RED} ;
`L_GREEN: {tload, tin, light, done, next1} =
{tdone & !on, `T_YELLOW, `GREEN, tdone,
(tdone & !on) ? `L_YELLOW : `L_GREEN} ;
`L_YELLOW: {tload, tin, light, done, next1} =
{tdone, `T_RED, `YELLOW, 1'b1, tdone ? `L_RED : `L_YELLOW} ;
default: {tload, tin, light, done, next1} =
{tdone, `T_RED, `YELLOW, 1'b1, tdone ? `L_RED : `L_YELLOW} ;
endcase
end
assign next = rst ? `L_RED : next1 ;
endmodule
依照timer時間變化紅綠燈
適時控制timer的倒數值，
決定紅綠燈秒數

## Slide 29: The Combiner
Notify master when legal to change (green, able to go red)
  ok = on & done
Trigger a red light when master changes direction
  on = (dir == cur_dir)
Update the current direction to input dir when all lights are red and able to go green
  next_dir = (!on & !done) ?
  dir : cur_dir
Trigger a green light when cur_dir has been updated
  on = (dir == cur_dir)
Output red lights for the two directions that are not cur_dir
Notes: 目前綠燈，可以改變燈號方向
當改變燈號方向，可以Trigger 紅燈，
更新目前方向
當目前方向改變，可以從紅燈變綠燈
當目前方向改變，trigger 綠燈
當方向和目前state 方向不一致，輸出紅燈

## Slide 30
//----------------------------------------------------------------------
// Combiner -
// dir - direction request from master FSM
// ok - acknowledge to master FSM
// lights - 9-bits to control traffic lights {NS,EW,LT}
//----------------------------------------------------------------------
module TLC_Combiner(clk, rst, dir, ok , lights) ;
input clk, rst ;
input [1:0] dir ;
output ok ;
output [8:0] lights ;
wire done ;
wire [2:0] light ;
reg [8:0] lights ;
wire [1:0] cur_dir ;
// current direction register
DFF #(2) dir_reg(clk, next_dir, cur_dir) ;
// light FSM
TLC_Light lt(clk, rst, on, done, light) ;
// request green from light FSM until direction changes
wire on = (cur_dir == dir) ;
// update direction when light FSM has made lights red
wire [1:0] next_dir = rst ? 2'b0 : ((!on & !done) ? dir : cur_dir) ;
// ok to take another change when light FSM is done
wire ok = on & done ;
// combine cur_dir and light to get lights
always @(cur_dir or light) begin
case(cur_dir)
`M_NS: lights = {light, `RED, `RED} ;
`M_EW: lights = {`RED, light, `RED} ;
`M_LT: lights = {`RED, `RED, light} ;
default: lights = {`RED, `RED, `RED} ;
endcase
end
endmodule
選到的方向，根據規則變化紅綠燈
其它沒選到的都紅燈

## Slide 31: Waveforms from simulation of factored machine
Notes: 東西向有車，燈號控制ok 可變綠燈，master fsm 設定方向為東西向 (01)
Combiner 要求目前方向的燈號變紅燈
慢慢變黃燈
Car_ew asserted, ok goes high, master FSM set dir to 01 (east_west)
Combiner set On low to request light FSM to set current direction’s light to go to red
Light FSM in turn responds by transitioing to the YELLOW state (10),
Once Light timer counter down, set done to 0
When done and on both go low, set current dir to east-west 01, go for another G-Y-R turn
After that, second ok pulse, ready for north-south, set dir to 0

## Slide 32: Summary
Factoring state machines
  Separate state into multiple ‘orthogonal’ state variables
  Each is simpler to handle (fewer states)
  Total number of states is product of numbers of sub-states
  “Factors out” repetitive sequences
  Hierarchical structure