## Slide 1: Digital Circuits and Systems Lecture 10 Synthesis
Tian Sheuan Chang

## Slide 2: Synthesis overview
Slides from Prof. Hung Ming Chen

## Slide 3: HDL-Based Design Flow

## Slide 4: Levels of Design
Notes: 3 domain
Behavior domain : focus on describing function, behavior . Do not care implementation details
Structural domain: focus on interconnection of components
Physical domain: focus on how to manufacture
Abstract level: system, RTL, logic, circuit according to design abstraction
Design usually goes through Behavior Structural and physical by using design aided tools indicated by arrows
Our thesis focus on RTL synthesis

## Slide 5: Register Transfer Level Synthesis
Synthesis = Domain Translation + Optimization
--VHDL //Verilog
if(A=‘1’) then if(A==1)
Y<=C + D; Y=C + D;
elseif (B=‘1’) then else if(B==1)
Y<=C or D; Y=C | D;
else Y<=C; else Y=C;
endif
+
Domain
translation
Optimization
(area, timing, power...)
Behavioral domain
Structural domain

## Slide 6: Two-Level Logic Optimization
Two-level logic representations
  Sum-of-product form
  Product-of-sum form
Two-level logic optimization
  Key technique in logic optimization
  Many efficient algorithms to find a near minimal representation in a practical amount of time
  In commercial use for many years
  Minimization criteria: number of product terms
Example: F = XYZ + XYZ + XYZ + XYZ+XYYZ
F = XY + YZ

## Slide 7: Multi-Level Logic Optimization
Transforms a combinational circuit to meet performance or area constraints
  Two-level minimization
  Common factors or kernel extraction
  Common expression re-subsitution
In commercial use for many years
Example:
f1 = abcd + abce +abcd + abcd +
ac + cdf + abcde + abcdf
f2 = bdg + bdfg + bdg + bdeg
f1 = c (a + x) + acx
f2 = gx
x = d (b + f) + d (b + e)

## Slide 8: Technology Mapping
Goal: translation of a technology independent representation (e.g. Boolean networks) of a circuit into a circuit in a given technology (e.g. standard cells) with optimal cost
Optimization criteria:
  Minimum area
  Minimum delay
  Meeting specified timing constraints
  Meeting specified timing constraints with minimum area
Usage:
  Technology mapping after technology independent logic optimization
  Technology translation

## Slide 9: Timing Optimization
There is always a trade-off between area and delay
Optimize timing to meet delay spec. with minimum area

## Slide 10: RTL Synthesis

## Slide 11: Domain Translation
Consistent with data
manipulation functions
Consistent with special semantics
x = y op z
optimization
(area, timing …)
Input HDL
Description
3-address
Code
Initial
Structural
Netlist
Combinational
Circuit
Generation
Special Element
Inferences

## Slide 12: Combinational Circuit Generation
Input HDL
Modified
3-address code
Functional unit allocation
Final result
Interconnection binding
computed by control/
data flow analysis

## Slide 13: Special Element Inferences
Given an HDL at RTL, three special elements need to be inferred to keep the special semantics in the HDL.
  Latch (D-type) inference
  Flip-Flop (D-type) inference
  Tri-state buffer inference
reg Q;
always@(D or en)
if(en) Q = D;
Latch is needed!!
reg Q;
always@(posedge clk)
Q <= D;
Flip-flop is needed!!
reg Q;
always@(D or en)
if(en) Q = D;
else Q = 1’bz;
Tri-state buffer
is needed!!

## Slide 14: Typical Latch Inference
Conditional assignments are not completely specified
  Check if the else-clause exists
Outputs conditionally assigned in an if-statement are not assigned before entering or after leaving the if-statement
always@(D or S)
if(S) Q = D;
always@(S or A or B)
begin
Q = A;
if(S) Q = B;
end
Do not infer latch
for Q
Infer latch
for Q

## Slide 15: Typical Latch Inference
Unreasonable limitations on coding style
always@(a or en)
if(en) x=a;
Wrong
circuit!
always@(a or en)
if(en) x=a;
else x=x;
Latch description

## Slide 16: Terminology
Clocked statement: edge-triggered always statement
  Simple clocked statement
  e.g., always @ (posedge clock)
  Complex clocked statement
  e.g., always @ (posedge clock or posedge reset)
Flip-flop inference must be conducted when synthesizing the clocked statements

## Slide 17: Typical Flip-Flop Inference on Simple Clocked Statements
Infer a flip-flop for each variable being assigned in the simple clocked statement
used after defined
connected to input of x
used before defined
connected to output of z

## Slide 18: Typical Flip-flop Inference on Complex Clocked Statements
Require the following syntactic template
  An if-statement immediately follows the always statement
  Each variable in the event list except the clock signal must be a selective signal of the if-statement
  Assignments in the blocks B1 and B2 must be constant assignments (e.g., x=1, etc.)
always @ (posedge clock or posedge reset or negedge set)
if(reset) begin B1 end
else if ( !set) begin B2 end
else begin B3 end

## Slide 19: Typical Flip-flop Inference on Complex Clocked Statements
Reset flip-flop
  The output Q changes to reset value i if
    The reset signal R = 1
    If R = 0, reset flip-flop = D flip-flop

## Slide 20: Typical Flip-flop Inference on Complex Clocked Statements
An example
Disadvantages
  Syntactic template results in unreasonable limitations in coding style
always @ (posedge clk or posedge R)
if(R) Q = 0;
else Q = D;
always @ (posedge clk or posedge R)
begin
Q = D;
if(R) Q = 0;
end
Non-synthesizable

## Slide 21: Typical Tri-state Buffer Inference
If a data object Q is assigned a high impedance value ‘Z’ in a multi-way branch statement (if, case, ?:)
  Associated Q with a tri-state buffer
  If Q associated with a tri-state buffer has also a memory attribute (latch, flip-flop)
    Real hardware cannot propagate Hi-Z (Hi-Z propagation problem)
    Place two memory elements to the control and the data inputs of tri-state buffer

## Slide 22: Synthesis Scripts

## Slide 23: Synthesis in design flow
Synthesis
  Tool: Design compiler (synopsys)
  Goal
    Model translation from RTL to gate-level
    Technology mapping
    Constrained optimization
Timing/area/power analysis
  Tool: Design Compiler, PrimeTime, PrimePower (synopsys)
  Goal
    Hardware performance verification
Gate-level simulation
  Tool: ncverilog (cadence)
  Goal
    Functionality verification
Specification
Algorithm Development (C/C++)
Architecture Design
RTL Coding
Synthesis
Gate-level Simulation
Timing/Area/Power Analysis
Auto-Place and Route
Post Simulation

## Slide 24: Data flow in Design Compiler
What you need to prepare:
  RTL codes
  Synthesis script
  Gate-level testbench
Design Compiler
Synthesis script (tcl)
RTL code
RTL code
RTL code
(.v)
DesignWare Library
Memory Model
(.db)
Gate-level Model
(.v)
Standard Delay Format file
(.sdf)
ncverilog
Gate-level Library
Performance report
Performance report
Performance Report
Technology Process Library
PASS or FAIL
Gate-level Testbench
(.v)

## Slide 25: Introduction to Design Compiler
Design Compiler (dc)
  Kernel of synthesis tool
Command-line interface
  Easy to iterative compiling
  dc_shell: original command of DC
  dc_shell-t: dc_shell + tcl (tool command language)
Menu-driven interface
  Friendly GUI interface
  Design Vision (dv) supports dc_shell and dc_shell-t
  Design Analyser (da) only supports dc_shell
  Open tools by command
    dv &
    da &
Before learning DC, you should learn the tcl first.

## Slide 26: Synthesis Script in DC

## Slide 27: Flow
First, select a semiconductor vendor
  TSMC
  UMC
  others
Default setting: .synopsys_dc.setup
  Search directory
    Synopsys root directory
    Home directory
    Working directory (highest priority)
  3 files are executed automatically.
  Viewed by command ls –la
1. Specify Library
2. Read Design
4. Define Design Environment
5. Set Design Constraint
6. Set Compile Strategy
7. Optimization
8. Analyze Design Problems
10. Save Design
9. Change Naming Rules
3. Create Clock

## Slide 28: 1. Specify library
Search path
  lists all the related directories of design and libraries.
  Syntax: set search_path {“…“}
Link library
  lists all technology process libraries with various timing condition.
  Syntax: set link_library {“wc.db” “bc.db”}
Target library
  selects libraries from link_library.
  Syntax: set target_library {“wc.db” “memory.db”}
Symbol library
  defines symbols of schematic view for DV or DA.
  Syntax: set symbol_library file.sdb
DesignWare library
  defines built-in operators in Synopsys
  Syntax: set synthetic_library {“dw_foundation.sldb”}

## Slide 29: Related libraries in our Lab
Technology process library
  Path: /CAD/UMC0090/UMC90_CELL/UMC90_CELL/SP_RVT_C05/synopsys
  File: l90sprvt_wc.db, l90sprvt_typ.db, l90sprvt_bc.db
Memory library
  Path: ../lib
  File: memory.db
Symbol library
  Path: /CAD/synopsys/synthesis/cur/libraries/syn
  File: generic.sdb
DesignWare library
  Path: /CAD/synopsys/synthesis/cur/libraries/syn
  File: dw_foundation.sldb
All the libraries’ path and name will be changed due to different technology processes and different tool versions.

## Slide 30: Set max/min libraray
Set an alternate library for min/max delay analysis.
  Command:
    set_min_library max_lib –min_verison min_lib
Libraries should be described in link_library.
Priority of delay value
  Delay in min library (higher)
  Delay in max library
set BEST_LIB(slow.db) fast.db
…
if [array exist BEST_LIB] {
echo "setting min/max libraries."
foreach lib_w [array names BEST_LIB] {
set lib_b $BEST_LIB($lib_w)
set_min_library $lib_w -min_version $lib_b
}
}

## Slide 31: 2. Read design
Supported format
  Verilog, VHDL, SystemVerilog
  Synopsys internal database format (.db, .ddc)
  Berkeley Escpresso format (.pla)
Method1:
  analyze (only HDL)
    Read HDL source files, check errors.
    Create and store HDL-independent intermediate objects.
  elaborate (only HDL)
    Translate intermediate objects into technology-independent design (GTECH).
    Load parameters in HDL source files.
    Replace DesignWare components.
    Execute link command to resolve design references.
Method2:
  read_file
    Read files with selected format.
    Execute the same steps in analyze and elaborate (without link and loading param.).
    Do not create intermediate objects (default).
    Ex1: read_file –rtl -format verilog $RTL
    Ex2: read_file –netlist -format verilog $GATE_LEVEL

## Slide 32: Set current design
Only one design can be set as current design for optimization.
Setting current design ways:
  Automatic setting after command
    read_file
    elaborate
  Direct command:
    current_design design_name

## Slide 33: Link design
Liking design (resolving references) is to connect all library components and design its references.
Command:
  link
Performed steps:
  libraries to reference
    local_link_library (highest priority)
    link_library
    search_path (lowest priority)
  reference to design

## Slide 34: 3. Create clock
Creating clock
  Command:
    create_clock -name name -period value -waveform {Tr, Tf} port
  Default clock characteristics (ideal clock)
    0 delay at clock port
    0 propagation delay
    0 transition delay
    0 uncertainty
  Ex:
    create_clock –period 5.0 –waveform {1.0, 2.0} [get_ports CLK2]

## Slide 35: Clock network effects
Clock latency
  consists of
    Source latency: clock source to clock pin
    Network latency: clock pin to register clock pin
Clock uncertainty (skew)
  Maximum differences between the arrival of clock signals at registers
Transition time
  It takes for a signal to change from low to high, or high to low.
  Transition time of input affects
    Delay to output
    Transition time of output

## Slide 36: Clock latency: network latency
Network latency
  Command:
    set_clock_latency delay [get_clocks clk]
    set_clock_latency -fall delay [get_clocks clk]
    set_clock_latency -rise delay [get_clocks clk]
  Option
    Rise: latency setting to only rising edges of clocks
    Fall: latency setting to only falling edges of clocks

## Slide 37: Clock latency: source latency
Source latency
  Command:
    set_clock_latency delay –source [get_clocks CLK]
    set_clock_latency delay –source -early [get_clocks CLK]
    set_clock_latency delay –source -late [get_clocks CLK]
  Option
    -early: for setup time checking
    -late: for hold time checking
  Ex
    set_clock_latency 1.5 –source –early [get_clocks CLK]
    set_clock_latency 2.5 –source –late [get_clocks CLK]

## Slide 38: Clock uncertainty
Difference in delay due to clock tree or multiple clock domains.
Two uncertainties:
  Single clock uncertainty
    set_clock_uncertainty delay[get_clocks CLK]
  Interclock uncertainty
    set_clock_uncertainty delay –from [get_clocks CLK1] –to [get_clocks CLK2]

## Slide 39: Clock transition time
Command:
  set_clock_transition delay [get_clocks CLK]
  set_clock_transition delay –fall [get_clocks CLK]
  set_clock_transition delay –rise [get_clocks CLK]
Option
  Rise: transition time setting to only rising edges of clocks
  Fall: transition time setting to only falling edges of clocks

## Slide 40: 4. Define design environment
Design environment
  Operating condition
    temperature
    supply voltage
    manufacturing process
  Wire load model
  System interface characteristics
    input drive
    input/output load
    fanout load

## Slide 41: Operating condition
General operating conditions in technology process
  best case (fast)
  typical case
  worst case (slow)
List available operation condition (library should be link before.)
  Command
    read_file my_lib.db
    report_lib my_lib
Specify operating condition
  Command
    set_operating_conditions op_name -library library_name
    set_operating_conditions -max wost_op -min best_op
set WORST_OP "slow"
set BEST_OP "fast“
…
if [array exist BEST_LIB] {
set_operating_conditions -max $WORST_OP -min $BEST_OP
} else {
set_operating_conditions -max $WORST_OP
}

## Slide 42: Wire load model
Wire load model is defined in library.
Wire effect estimation
  wire length
  fanout
3 Hierarchical wire load modes
  Top (most rough estimation)
    no subdesigns’ wire load models
  Enclosed
    depends on its level
  Segmented (most accurate estimation)
    depends on its positions.

## Slide 43: Wire load mode (cont.)
List available wire load models
  Command
    read_file my_lib.db
    report_lib my_lib
Specify wire load models
  Command
    set_wire_load_model -name model_name -library lib_name
    set_wire_load_mode mode_name

## Slide 44: Concept of transition time, drive strength
Transition time
  is set as constant(rough model).
  is set as function of RC (accurate model).
    Tobj = Tprev + R x C
Drive strength (default: infinite)
  Drive strength = 1 / R
  The selected cell should have the drive strength more than required one.
Transition time Tobj
Tprev
R
C
Tobj
Tprev

## Slide 45: System interface
Drive cell
  is defined in technology library.
  Command: set_drive_cell –lib_cell cell IN
Drive strength
  is set for the inputs of design.
  Command: set_drive R IN
Input transition delay
  Rough setting
  Command: set_input_transition time IN
Load on input/output (capacitance)
  Output load: is used to select proper cell drive strength
  Input load: is used to model transition delay
  default: 0
  command: set_load C IN/OUT/NET

## Slide 46: System interface: input/output port
Fanout effect
  No unit
  Fanout_load and max_fanout of each cell are defined in technology library.
  Constraint
    ∑fanout_load <= max_fanout
  Command: set_fanout_load value OUT

## Slide 47: 5. Set design constraints
Two types of constraints in DC
  Design rule constraints (precedence)
    include
      max. transition time
      max. fanout
      max/min. capacitance
    are defined by technology library.
    can be defined more restrictively by designer.
  Optimization constraints
    include
      area
      speed
    are defined by designer.

## Slide 48: Design rule constraints
Max transition time (ns)
  is the longest time to drive a pin and change its value.
  command: set_max_transition time IN/OUT/design
Max fanout (no unit)
  ∑fanout_load <= max_fanout
  A high drive strength cell has higher fanout.
  command: set_max_fanout value IN/design
Max capacitance
  is total capacitive load(net) that an output pin can drive.
  command: set_max_capacitance C IN/OUT/design
Min capacitance
  specifies min load that a cell drive.
  command: set_min_capacitance C IN
Typical design rule scenarios
  set_max_fanout + set_max_transition
  set_max_fanout + set_max_capacitance

## Slide 49: Optimization constraints
Timing constraint
  sets input delay on pins or input/output ports relative to a clock signal.
  command: set_input_delay delay –clock clock in
  command: set_output_delay delay –clock clock out
Max area
  unit: number of gates, instead of physical area
  ignored components in optimization
    unknown components
    components with unknown area
    technology-independent generic cells
  command: set_max_area area
  area = 0 (as small as possible)

## Slide 50: 6. Select compile strategy
Three compile strategies
  Top-down compile
  Bottom-up compile
  Mixed compile
Methods for resolving instances
  Uniquify method
  Compile-once-don’t-touch method
  Ungroup method

## Slide 51: Uniquify method
Create a unique design for each instance, even if it is resolved from an identical reference.
Command:
  uniquify
  uniquify –cell cell_name
Pros and cons
  more memory
  longer compile time
  better performance
Hierarchy in cell is preserved.

## Slide 52: Compile-once-don’t touch method
Pre-compile sub-designs, and set it as don’t touch for compiling entire design.
Command
  set_dont_touch cell_list
Pros and cons
  less memory
  shorter compile time

## Slide 53: Ungroup method
The same effect as uniquify method but it removes hierarchical levels.
Command
  ungroup cell_list
Pros and cons
  more memory than compile-once-don’t-touch
  longer compile time than compile-once-don’t touch
  better performance
  It removes user-defined design heirarchy
Hierarchy in cell is broken.

## Slide 54: 7. Optimization
DC performs 3 optimization levels
  Architectural optimization on HDL descrition
    Sharing common expressions
    Sharing resources
    Selecting DesignWare implementations
    Reordering operators
    Identifying arithmetic expressions for data-path synthesis (DC-ultra)
  Logic-level optimization on GTECH netlist
    Structuring
    Flattening for conditional logic
  Gate-level optimization on technology-dependent netlist
    Technology mapping
    Delay optimization
    Design rule fixing
    Area optimization

## Slide 55: compile
Default synthesis algorithm
  command
    compile
    compile –map_effort median –area_effort median
Advanced synthesis algorithms
  High-performance designs
    compile_ultra
  Maximum performance
  Minimum area
  Data path
More information
  Refer to “Design Compiler Optimization Reference Manual”

## Slide 56: 7. Analyze design problems

## Slide 57: Area
Analyzing area
  Combinational area
  Non-combinational area
  Total area
Report for current design
  report_area
Report for current design across the hierarchy
  report_area -heirarchy
****************************************
Report : area
Design : JBF
Version: B-2008.09-SP2
Date : Wed Dec 23 20:38:36 2009
****************************************
Library(s) Used:
……
Number of ports: 169
Number of nets: 70269
Number of cells: 55211
Number of references: 205
Combinational area: 669475.743010
Noncombinational area: 1593732.288294
Net Interconnect area: 13561542.382202
Total cell area: 2263208.031303
Total area: 15824750.413506

## Slide 58: Timing
report_design
  Shows operating conditions, wire load model and mode, timing ranges, internal input and output, and disabled timing arcs.
check_timing
  Checks for unconstrained timing paths and clock-gating logic.
report_port
  Shows unconstrained input and output ports and port loading.
report_timing_requirements
  Shows all timing exceptions set on the design.
report_clock
  Checks the clock definition and clock skew information.
report_path_group
  Shows all timing path groups in the design.
report_timing
  Checks the timing of the design.
  Slack should be 0 or positive.
report_constraint
  Checks the design constraints.
report_delay_calculation
  Reports the details of a delay arc calculation.

## Slide 59: redirect command
Dump the result of a command into a file
Command:
  redirect output_file {command}
Ex
  redirect [format "%s%s" $TOP "_syn_area.rpt"]{report_area}
redirect [format "%s%s%s" "REPORT/" $TOP "_syn_min_timing.rpt"] { report_timing -delay min -max_paths 10 }
redirect [format "%s%s%s" "REPORT/" $TOP "_syn_max_timing.rpt"] { report_timing -delay max -max_paths 10 }
redirect [format "%s%s%s" "REPORT/" $TOP "_syn_area.rpt"] { report_area }
redirect [format "%s%s%s" "REPORT/" $TOP "_syn_constraint.rpt"] { report_constraint -all_violators -verbose }
redirect [format "%s%s%s" "REPORT/" $TOP "_syn_resources.rpt"] { report_resources -hierarchy }

## Slide 60: 8. Change naming rule
Goal
  Change naming rule in netlist to avoid confliction in APR.
Variables
  bus_inferface_sytle
    individual bits of bus
  bus_naming_style
    individual port member, net member, or cell instance
  hdlout_internal_busses
    internal bused nets by parsing the names of the nets.
set bus_inference_style {%s[%d]}
set bus_naming_style {%s[%d]}
set hdlout_internal_busses true

## Slide 61: Change naming rule (cont.)
change_name
  Changes the names of ports, cells, and nets in a design.
  -hierarchy: all names in the design hierarchy are to be modified.
  -rule verilog: bulit-in verilog naming rules
  -rule name_rule: user-defined naming rules
define_name_rules object …
  -allowed: allowed charaters
  -max_length: allowed max length of name
  -map: replace string in name
    Ex: replace \*cell*\ by cell
change_names -hierarchy -rule verilog
define_name_rules name_rule -allowed {a-z A-Z 0-9 _} -max_length 255 -type cell
define_name_rules name_rule -allowed {a-z A-Z 0-9 _[]} -max_length 255 -type net
define_name_rules name_rule -map {{"\*cell\*", "cell"}}
change_names -hierarchy -rules name_rule

## Slide 62: 9. Save design
database (.db)
  Command: write –hierarchy –format db –output file.db
netlist (.v)
  IEEE standard Verilog
  Command: write –hierarchy –format verilog –output file.v
standard delay format (.sdf)
  Delay model for gate-level simulation
  Command: write_sdf –context verilog –version 1.0 file.sdf
standard parasitic extraction format(.spef)
  Netlist with RC information
  Command: write_parasitics –format reduced –output file.spef
  -format reduced: one resistance and one capacitance for net model
Synopsys design constraints (.sdc)
  Command: write_sdc file.sdc

## Slide 63: Gate-level simulation
Command
  ncverilog testbench –v tech_model.v +access+r
  tech_model.v
    Path: /CAD/UMC0090/UMC90_CELL/UMC90_CELL/SP_RVT_C05/verilog
    File: l90sprvt.v