## Slide 1: Digital Circuits and Systems Lecture 13 Interfaces, Interconnect, and Memory
資料要從一個模組傳到另一個模組，要如何溝通，告訴對方這是有效的資料?
Tian Sheuan Chang

## Slide 2: Outline [Dally. Ch. 22. 24. 25]
Interface Timing: sequencing the transfer of data
  安排資料怎麼傳
  從簡單到複雜的方式
Interconnect
  實體電路的樣子
  從簡單到複雜的方式
Memory
  先存起來，慢慢再用
Notes: 針對兩種傳資料方式討論
  一對一(點對點)傳遞資料
  多對多傳遞資料

## Slide 3: Recap: System on a Chip (SOC)
Source: ARM
Notes: Many systems include Analog and Digital functions.
This course will deal only with digital designs.

## Slide 4: Recap: Breakdown of Modern SOC Design
Core
  CPU/DSPs/GPUs
  Hardware accelerators (AI engine/video codec/MP3 codec)
  Complex data path + FSMs (pipeline/parallel)
Bus
  Connect core and peripherals
  MUX/arbiters
Peripheral
  Interface from/to the external
  speech/audio, camera/display, I2S/I2C, GPIO
  Serial to parallel, parallel to serial + FSM

## Slide 5: Recap: An Example AMBA System

## Slide 6: Recap: From C Array to Memory Access
http://www.phatcode.net/res/260/files/html/SystemOrganizationa2.html
Memory Write Operation
Memory Read Operation
CPU = Memory [125]
Memory [125] = 0

## Slide 7: Recap: How CPU access these I/O interface?
Memory mapped I/O (treat other components as memory)
Notes: https://www.chegg.com/homework-help/questions-and-answers/exercise-828-use-mips-memory-mapped-o-interact-user-time-user-presses-button-pattern-choic-q30535077
http://vegetableavenger.blogspot.com/2013/12/beagleboen-black-io-library-mmap.html

## Slide 8: Interface timing

## Slide 9: Interface Timing
How do you pass data from one module to another?
  Open loop: 資料送了就送了，有沒有收到是你家的事，繼續送下一筆
  Flow control: 資料送了，要有通關訊號 或 回條，才送下一筆
  Serialized: 通道狹窄，一次只能傳一個bit
  比較複雜的通常都是晶片外面溝通用，或大模組間使用，因為不確定高

## Slide 10: 簡單的方式 Always Valid Timing
(通常都是這種，晶片內部用較多，確定性高)
Dataum is valid every cycle, and can be sampled by the receiver at any time

## Slide 11: 簡單的方式 Periodically Valid Timing
通常會有一個data_valid 訊號，表示資料在data_valid ==1 那段時間有效，可以讀，規則時就省略
不規則出現會需要明白此訊號表示
No flow control, and values cannot be dropped or repeated
Need flow control to move the valid signal across clock domain

## Slide 12: 複雜的方式 Flow Control: ready-valid flow
Ready 或valid 兩者都為1
才能傳

## Slide 13: Flow-control
Valid – Tx has data available 傳送端資料是有效的
Ready – Rx able to take data 通關訊號，接收端可以收資料
特例
  Push flow control – assume Rx always Ready
  Pull flow control – assume Tx always Valid

## Slide 14: 複雜的方式 Serialization: USB, SATA, I2C, I2S
Frame signals start of new serial frame (in this case 4 words)
Flow control can be at frame granularity or word granularity
傳送開始
高頻或介面接腳數量有限狀況時，會用這個方法

## Slide 15: Serialization with word granularity FC
不能接收，資料要再延續下去

## Slide 16: 常見介面訊號
Control
  Read/write, sequential, non-sequential
Address
  讀寫位置
  特別是用於bus or memory
Data
  有時候會再細分成不同field，方便使用

## Slide 17: An Example AMBA System

## Slide 18: AHB Interconnect
Basic components:
Master
Slave
Arbiter
Decoder
Mux

## Slide 19: AHB Simple Transfer
Address control
Data
A
A
B
B
C
C
D
D
Two phases to complete an access as the pipeline
Address phase: lasts only a single cycle
Data phase: can be stretched for several cycles by slave
HCLK: Reference for all AHB activity
HADDR: 32 bit Address Bus
HWRITE: Read/Write cycle
HWDATA: Write Data Bus
HREADY: Transfer complete response
HRDATA: Read Data Bus

## Slide 20: AHB Transfer with Wait States
* Access is stretched by slave which keep HREADY deassert
* It is recommended, but not mandatory, that slave do not insert more than 16 wait states

## Slide 21: Multiple Transfers
Address & control
Data & Response
A
A
B
B
C
C
* Address phase of C is stretched because of stretched data phase of B

## Slide 22
Example without Interface
module top;
module memMod(input logic req,
logic req,gnt,start,rdy;
bit clk,
bit clk = 0;
logic start,
logic [1:0] mode;
logic[1:0] mode,
logic [7:0] addr,data;
logic[7:0] addr,
inout logic[7:0] data,
memMod mem(req,clk,start,mode,
output logic gnt,
addr,data,gnt,rdy);
cpuMod cpu(clk,gnt,rdy,data,
logic rdy);
req,start,addr,mode);
always @(posedge clk)
endmodule
gnt <= req & avail;
endmodule
Top
clk
module cpuMod(input bit clk, logic gnt,
req
logic rdy,
start
gnt
inout logic [7:0] data,
rdy
output logic req,
mode[1:0]
logic start,
CPU
Mem
addr[7:0]
logic[7:0] addr,
logic[1:0] mode);
data[7:0]
endmodule

## Slide 23
Example Using Interfaces
interface
Bundle signals
interface simple_bus;
module top;
instance
in interface
logic req,gnt;
bit clk = 0;
logic [7:0] addr,data;
simple_bus sb_intf;
Connect
logic [1:0] mode;
interface
logic start,rdy;
memMod mem(sb_intf, clk);
endinterface: simple_bus
cpuMod cpu(.b(sb_intf),
Use interface
.clk(clk));
endmodule
keyword in port list
module memMod(interface a,
Top
clk
input bit clk);
logic avail;
always @(posedge clk)
a.gnt <= a.req & avail;
sb_intf
endmodule
Refer to intf
CPU
Mem
signals
module cpuMod(interface b, input bit clk);
endmodule

## Slide 24: interconnection

## Slide 25: Interconnect 不只是一對一連接時，還能怎麼做?
Many clients need to communicate
Ad-hoc point-to-point wiring or shared interconnect
Like a telephone exchange

## Slide 26: 1. Bus:
Shared Interconnect
One sender/receiver pair allowed

## Slide 27: Verilog for a simple bus interface
// Combinational Bus Interface
// t (transmit) and r (receive) in signal names are from the perspective of the bus
module BusInt(cr_valid, cr_ready, cr_addr, cr_data, // bus rx - to the bus
ct_valid, ct_data, // bus tx - from the bus
br_addr, br_data, br_valid, // to the bus
bt_addr, bt_data, bt_valid, // from the bus
arb_req, arb_grant, // the arbiter
my_addr) ; // address of this interface
parameter aw = 2 ; // address width
parameter dw = 4 ; // data width
input cr_valid, arb_grant, bt_valid ;
output cr_ready, ct_valid, arb_req, br_valid ;
input [aw-1:0] cr_addr, bt_addr, my_addr ;
output [aw-1:0] br_addr ;
input [dw-1:0] cr_data , bt_data ;
output [dw-1:0] br_data, ct_data ;

## Slide 28
// arbitration
wire arb_req = cr_valid ; //client data valid
wire cr_ready = arb_grant ;//client ready
// bus drive
// assumes bus ORs these signals with those from other interfaces
wire br_valid = arb_grant ; //client get grant to send data
wire [aw-1:0] br_addr = arb_grant ? cr_addr : 0 ; //address
wire [dw-1:0] br_data = arb_grant ? cr_data : 0 ; //data
// bus receive
wire ct_valid = bt_valid & (bt_addr == my_addr) ; //if bus address==myaddr,
wire [dw-1:0] ct_data = bt_data ;
endmodule

## Slide 29: 2. Crossbar Switch:
全連接型態
可同時多個傳送
只要目的不同
Multiple sender/receiver pairs

## Slide 30: 3. Interconnection Networks (Network on Chip: NoC)
網路型
可以容忍更長時間延遲

## Slide 31: Interconnection Networks

## Slide 32: What factors determine which interconnect solution you pick?
Bandwidth scalability
  NoC > crossbar > bus
Cost
  Bus < crossbar < NoC

## Slide 33: memory

## Slide 34: Memory
Address
Data
Capacity
Bandwidth
Latency
Granularity

## Slide 35: SRAM
https://semiengineering.com/embedded-memory-impact-power-grids/
Notes: https://semiengineering.com/embedded-memory-impact-power-grids/

## Slide 36: SRAM Primitive

## Slide 37: DRAM Primitive
Address is split into Bank, row, column
三步驟存取: bank/row activation, column access, precharge
同一bank，changed to 不同row要先precharge
Notes: Address is split into Bank, row, column

## Slide 38: DRAM Operation

## Slide 39: 如果一塊memory大小不夠或bandwidth輸出入頻寬不夠，那怎麼辦? 一塊不夠，那就兩塊，或更多塊

## Slide 40: 增加容量: Bit-Slicing
輸出入bitwidth可以增加
4bit x 16 => 64bit

## Slide 41: 增加容量: Banking
一次只讀寫一個，其他可以關掉省電

## Slide 42: Bit slicing & banking
Multi-bank access
Each bank allows one read one write
For this example, 4 read/write port are allowed
The only limitation is different address

## Slide 43: 多個同時讀寫Interleaving
Multiple bank 另種用法: 讀寫多個，但位址不一樣，有彈性
M request to N memory bank
Dual port/multiport memory

## Slide 44: Avoid head-of-line blocking
若只能照順序讀寫，會被卡住
使用率低
不照順序讀寫，誰有空就去做
不會被卡住，使用率100%

## Slide 45: Hierarchy
容量小的速度快，放在靠近logic附近，容量大的速度慢，放在比較遠的地方
可以搭配cache

## Slide 46: Summary
Interface timing
  Convention about when data is transferred
    When valid, when accepted
    Open loop – always valid or periodic
    Ready-valid flow-control, both ways, push, or pull
  Serialization
Interconnect
  Allow any pair of clients to communicate
  Bus, Crossbar, Network
Memory
  Capacity, bandwidth, latency, and granularity
  SRAM and DRAM primitives
  Bit-slice bank, or interleave to combine primitives
  Hierarchy