## Slide 1: Outline
Introduction to hardware description language (HDL)
  Why it is better than schematic entry
Verilog語法 1 (Functional viewpoints)
  Modules and ports
  Basic syntax rules
  Structural Verilog
  How to model combinational logic
  How to model sequential logic
Verilog語法 2 (Language viewpoints)
  One language, many coding styles
  Continuous v.s. procedural assignments
  Blocking vs NonBlocking
  For loop and parameterized design
SystemVerilog
Gotchas 正確的使用方法 <= (會踩到的陷阱)
Notes: Here is a list of lecture objectives. They are provided for you to reflect on
what you are supposed to learn, rather than an introduction to this lecture.
I want, by the end of this lecture, to give you some idea about the basic
structure and syntax of Verilog. I want to convince you that schematic
capture is NOT a good way to design digital circuits. Finally, I want you to
appreciate how to use Verilog to specify a piece of hardware at different
levels of abstraction.

## Slide 2: SystemVerilog design enhancement (partial)

## Slide 3: SystemVerilog is a Huge Extension of Verilog

## Slide 4: SystemVerilog Means Productivity

## Slide 5: Increase Designer Productivity

## Slide 6: Single Language for Design and Verification: HDVL

## Slide 7: SystemVerilog Data Types

## Slide 8: Almost Universal Data Types: logic (or reg)
Logic is a better name than reg, so is preferred
Error code
assign a = b+ 1;
always_comb
a = d + 3;
Notes: assign a = b+ 1;
assign a = c+ 2;
always_comb
a = d + 3;

## Slide 9: Verilog 2001 Data Types

## Slide 10: Almost Universal Data Types: logic

## Slide 11: User Defined Types: typedef

## Slide 12: Design Strategy: Use All typedef’s

## Slide 13: Enhanced Literal Number Syntax

## Slide 14: Enumerated Data Types
Allow to define a datatype whose values have names
  Useful for state coding, op code, or symbolic data
By default, the first get the value 0
Notes: 列舉

## Slide 15: Port Instance and Port Connections

## Slide 16: .Name Implicit Port with SystemVerilog
Use .name if port name and interconnection wire name are the same
Port 名稱與接線名稱相同
寫port名稱就可以
Notes: Port 名稱與接線名稱相同
寫port名稱就可以

## Slide 17: .* Implicit Port with SystemVerilog
.* only needs to specify the difference
Notes: Port 名稱與接線名稱相同
用 .* 代替
不同的才寫

## Slide 18: Rule for .* and .name Connections
Notes: 大小不同
名字不同
空接

## Slide 20: Logic-Specific Processes

## Slide 21: SystemVerilog Interface

## Slide 22: What is an Interface?
Provides a new hierarchical structure
  Encapsulates interconnect and communication
  Separates communication from functionality
  Eliminates "wiring" errors
  Enables abstraction in the RTL

## Slide 23
Example without Interface
module top;
module memMod(input logic req,
logic req,gnt,start,rdy;
bit clk,
bit clk = 0;
logic start,
logic [1:0] mode;
logic[1:0] mode,
logic [7:0] addr,data;
logic[7:0] addr,
inout logic[7:0] data,
memMod mem(req,clk,start,mode,
output logic gnt,
addr,data,gnt,rdy);
cpuMod cpu(clk,gnt,rdy,data,
logic rdy);
req,start,addr,mode);
always @(posedge clk)
endmodule
gnt <= req & avail;
endmodule
Top
clk
module cpuMod(input bit clk, logic gnt,
req
logic rdy,
start
gnt
inout logic [7:0] data,
rdy
output logic req,
mode[1:0]
logic start,
CPU
Mem
addr[7:0]
logic[7:0] addr,
logic[1:0] mode);
data[7:0]
endmodule

## Slide 24
Example Using Interfaces
interface
Bundle signals
interface simple_bus;
module top;
instance
in interface
logic req,gnt;
bit clk = 0;
logic [7:0] addr,data;
simple_bus sb_intf;
Connect
logic [1:0] mode;
interface
logic start,rdy;
memMod mem(sb_intf, clk);
endinterface: simple_bus
cpuMod cpu(.b(sb_intf),
Use interface
.clk(clk));
endmodule
keyword in port list
module memMod(interface a,
Top
clk
input bit clk);
logic avail;
always @(posedge clk)
a.gnt <= a.req & avail;
sb_intf
endmodule
Refer to intf
CPU
Mem
signals
module cpuMod(interface b, input bit clk);
endmodule

## Slide 25: Outline
Introduction to hardware description language (HDL)
  Why it is better than schematic entry
Verilog語法 1 (Functional viewpoints)
  Modules and ports
  Basic syntax rules
  Structural Verilog
  How to model combinational logic
  How to model sequential logic
Verilog語法 2 (Language viewpoints)
  One language, many coding styles
  Continuous v.s. procedural assignments
  Blocking vs NonBlocking
  For loop and parameterized design
SystemVerilog
Gotchas 正確的使用方法 <= (會踩到的陷阱)
Notes: Here is a list of lecture objectives. They are provided for you to reflect on
what you are supposed to learn, rather than an introduction to this lecture.
I want, by the end of this lecture, to give you some idea about the basic
structure and syntax of Verilog. I want to convince you that schematic
capture is NOT a good way to design digital circuits. Finally, I want you to
appreciate how to use Verilog to specify a piece of hardware at different
levels of abstraction.

## Slide 26: Gotchas
Verilog 正確的使用方法 <= (會踩到的陷阱)
Notes: 容易踩到的陷阱

## Slide 27: Combinational Logic
initial value for combinational logic will be ignored for synthesis
No assign block (legal but not synthesizable)
WRONG!!!
logic a =0;
assign a=b+c;
硬體設計沒有起始值這種東西

## Slide 28: How to Properly Initialize a DFF?
Reset DFF registers
  You can reset DFF when rst_n triggers
  Do not use initial begin since it is not synthesizable
always_ff@(posedge clk or negedge rst_n)
if(rst_n == 0)
a <= 0;
else
a <= b;
initial a = 0;
logic a = 0;
Bad for design, not synthesizable
Only for testbench simulation
Initial values are ignored for synthesis

## Slide 29: Combinational Loop
A variable cannot be assigned by itself in combinational logic
  Combinational loop (timing loop)
WRONG!!! Not synthesizable
Same variable in both sides
always_comb
a = b+a;
always_ff@(posedge clk)
a <= b+a;
Same variable in both sides
only allowed in seq. logic

## Slide 30: Multiple Drivers
Multiple driver
  One variable can only be assigned in one always block or in one assign
  This will cause race conditions (actual values depends simulator scheduling)
  Solution: multiple source statements should put in the same always or assign
always_comb
a = e+f;
always_comb
a = 2;
assign a=c+d;
assign a=4;
always_comb bein
a = e+f;
a = 2;
end
Same for initial statement
and always_ff
Initial //at t=0
a = 1;
Initial //at t=0
a = 0;
logic a = 1;

## Slide 31: Same variable used in two loops running simultaneously
Index variable i in both loops will conflict

## Slide 32
Use local variable within for loop

## Slide 33: Sizing in Verilog
Verilog automatically resizes values in an expression according to the sizes of variables in the expression.
Verilog automatically truncates or extends the right-hand-side value in an assignment to fit the left-hand-side variable.
  module sign_size;
  reg [3:0] a, b;
  reg [15:0] c;
  initial
  begin
  a = -1; // a is unsigned, so it stores “1111”
  b = 8;
  c = 8; // b = c = 1000
  #10 b = b + a; // result 10111 is truncated. b = 0111
  #10 c = c + a; // c = 0000000000010111
  end
  endmodule

## Slide 34: Sizing in Verilog
Self-determined versus context-determined operators
context-determined operator
  looks at the size and data types of the complete statement before performing its operation. All operands in the statement are expanded to the largest vector size of any operand before the operations are performed
logic [5:0] a = 6'b010101; II 6-bit vector
logic [3:0] b = 4'b1111; II 4-bit vector
logic [7:0] c; II 8'bit vector
c = a & b; II results in 8-bit 00000101
Notes: Gotcha 44
In this example, the context of the bitwise AND operation includes the vector
sizes of a, band c. The largest vector size is 8 bits. Therefore, before doing the
operation, the 4-bit vectorandthe 6-bitvector are expanded to 8-bitvectors.
Why were a andb left extended with zeros? Thisquestion is answered in Gotcha
46 on page 105, which discusses zero-extension andsign-extension in Verilog,

## Slide 35
A self-determined operator
  is only affected by the data types of its operands. The operation is not affected by the context in which it is performed. For example, a unary AND operation will AND all the bits of its operand together, without changing the size of the operand.
logic [5:0] a = 6'b101010; // 6-bit vector
logic [3:0] b = 4'b1111; // 4-bit vector
logic [7:0] c; //8'bit vector
c = a I (&b); // results in 8-bit 00101011
Notes: In this example, the unaryANDof o ( &b) is self-determined. Thevector sizesof
a and c haveno bearing on the unaryAND of'b, Theresultof ANDing the bits of
4 ' b 1111 together is a 1 ' b 1.
If the self-determined operator is part of a compound expression, as in the
example above, then the result of the self-determined operator becomes part of
the context for the rest of the statement.
What if &bhadbeencontext-determined? In context, b would firstbe expanded to
8 bits wide, becoming 00001111. TheunaryAND of this value is 1 ' b 0, instead
of l' b1. The result of a I &b would be 00101010, which would be the wrong
answer. But this is not a gotcha, because the unary AND operator is selfdetermined,
and therefore gets the correct answer.

## Slide 36: Imcompleted case / if-else => unintentional latch
module mux4( input a, b, c, d
input [1:0] sel,
output out );
reg out;
always @( * )
begin
if ( sel == 2’d0 )
out = a;
else if ( sel == 2’d1 )
out = b
else if ( sel == 2’d2 )
out = c
else if ( sel == 2’d3 )
out = d
//else
// out = 1’bx;
end
endmodule
module mux4( input a, b, c, d
input [1:0] sel,
output out );
reg out;
always @( * )
begin
case ( sel )
2’d0 : out = a;
2’d1 : out = b;
2’d2 : out = c;
2’d3 : out = d;
//default : out = 1’bx;
endcase
end
endmodule
6.375 Complex Digital Systems
Nested if-else
case

## Slide 37: How to Find Incomplete Case/if-else
Code review
By tools
  Linting tools: nLint (renamed as Synopsys Spyglass Lint)
  Synthesis tools: check “latch” keyword in the synthesis log
    Compiler generates warning messages when inferring latches

## Slide 38: SpyGlass(renamed from nLint) rule(1)
Simulation
  Combinational Loop
  Infinite Loop
  Signal in Sensitivity List Changed in the Block
  Loss of Significant Bit
Synthesis
  Logic Expression Used in Sensitivity
  Delay in Non-blocking Assignment
  Blocking/Non-blocking Assignment in Edge-triggered Block
  Inferred Latch
ERC
  Floating Net
  Partial Input Floating
  Output Floating
  Input Floating
DFT
  Gated Clock
  Buffered Clock
  Reset Driven by Combinational Logic

## Slide 39: nLint rule(2)
Design Style
  Two-process Style Not Used for FSM
  Clock Driven by Sequential Logic
  Clock Signal Used on Both Edges
  No Set or Reset Signal
  No Glue Logic Allowed in Top Module
Language Construct
  Bit Width Mismatch in Assignment
  Multi-bit Expression when One Bit Expression is Expected
  Bit Range Specified for Parameter
  Bit Width Mismatch Between Module Port and Instance Port
HDL Translation
  Verilog/VHDL Reserved Words
  Include Compiler Directive Used
Naming Convention
  Port Name Too Long
  Clock Name Prefix or Suffix
  Active Low Signal Name Prefix or Suffix
  Port Name Does Not Follow the Connected Signal

## Slide 40: nLint rule(3)
Coding Style
  Line Too Long
  TAB Used in Indentation
  More than One Statement per Line
  Unconventional Port Declaration Order
VITAL Compliant
  For VHDL only
Clock
  Generated Reset
  Generated Clock
  Tri-state Buffer in a Clock Path
Block Interconnect
  Conflict of Hierarchy Interconnection
  Block Assembly Error in the Same Hierarchy Level

## Slide 41: Blocking vs. non-blocking assignment
Blocking assignment (for combinational circuit)
  The assignment will be carried consequently.
Non-blocking assignment (for sequential circuit)
  The assignment will be carried in parallel.
always@( posedge clk )
begin
b = a;
c = b;
end
always@( posedge clk )
begin
b <= a;
c <= b;
end
Blocking
Non-blocking
T=0
a=2,
b=1
Notes: 假設在a=2 的clock

## Slide 42: Blocking vs. non-blocking assignment
reg
c
a
reg
reg
b
a
always@( posedge clk )
begin
b = a;
c = b;
end
always@( posedge clk )
begin
b <= a;
c <= b;
end
Blocking
Non-blocking
c

## Slide 43: Value Swap
initial begin
x = 5;
y = 3;
end
always @(negedge clock) begin
x = y;
y = x;
end
always @(negedge clock) begin
x <= y;
y <= x;
end
This will give both x and y the same value.
Race condition: If the circuit was to be built a race condition has been entered which is unstable. The compliler will give a stable output, however this is not the output expected.
The simulator assigns x the value of 3 and then y is then assigned x. As x is now 3, y will not change its value.
both the values of x and y are stored first. Then x is assigned the old value of y (3) and y is then assigned the old value of x (5)
Notes: http://xilinx.pe.kr/_hdl/2/RESOURCES/www.ee.ed.ac.uk/~gerard/Teach/Verilog/me5cds/me95jpbh.html

## Slide 44: (Don’t) Mix Blocking and NonBlocking
always @ (posedge clk) begin
if(shiftIndex == 0) begin
if(dataValid == 1) transmitting = 1; //Blocking assign
else transmitting = 0; //Blocking assign
end
if(transmitting == 1) begin
shiftIndex <= shiftIndex + 1;
dataOut <= data5b[shiftIndex];
if(shiftIndex == 4) begin
complete <= 1;
shiftIndex <= 0;
end
else begin
complete <= 0;
end
end
end
always @* begin
if(shiftIndex == 0) begin
if(dataValid == 1) transmitting = 1; //Blocking assign
else transmitting = 0; //Blocking assign
end
end
always @ (posedge clk) begin
if(transmitting == 1) begin
shiftIndex <= shiftIndex + 1;
dataOut <= data5b[shiftIndex];
if(shiftIndex == 4) begin
complete <= 1;
shiftIndex <= 0;
end
else begin
complete <= 0;
end
end
end
//only evaluated on positive clock edge
Notes: When using the blocking (=) assignment the value is available to use in the next line of code. This implies it is combinatorial and not driven from a flip-flop.
In simulation it looks like it is driven from a flip-flop because the block is only evaluated on positive clock edge, in reality it is not which might break the interface.
I am of the faction which says never mix styles, as it can be a problem in code reviews and refactoring. The refactor, if a module needs to output a new signal and it is seen that it already exists they just change to be an output. At first glance looked like it was a flip-flop because it was in a always @(posedge clk block.
Therefore I would recommend to NOT mix styles, but pull out the section that is combinatorial and put it in its own block. Does this still meet your requirements? if not then you would have had problem.
I do not see how data valid is controlled but it can change the output transmitting, potentially transmitting could also glitch as it is from a combinatorial decode, not driven cleanly from a flip-flop. The receiving interface might be async, glitches could cause lock up etc.
https://stackoverflow.com/questions/28599018/mixing-blocking-and-non-blocking-assign-in-verilog-or-not

## Slide 45
Race Condition Using Blocking Assignments
Notes: Presto Verilog does not permit this and generates an error message.

## Slide 46: Tri-State Logic
If possible, use multiplexors to replace tri-state logic
  Used for bidirectional I/O pad
How to write tri-state logic?
// module declaration
module tri_state_buffer( data_in, data_out, data_pad, ctrl);
// port declaration
input [15:0] data_in;
input ctrl;
output [15:0] data_out;
inout 15:0] data_pad;//bidirectional port
// structure
assign data_pad = (ctrl)? data_in : 16’hz;
assign data_out = data_pad;
endmodule

## Slide 47: Tri-State Logic
Use in on-chip bus or I/O pad

## Slide 48: Verilog Modeling Style for Synthesis

## Slide 49: Quick Glimpse of Synthesizable Subset
always | begin end | case endcase | casez endcase
if else | module endmodule | input output | function
reg Wire logic | default | posedge negedge | parameter
or | assign | for | 
Not all of the Verilog commands can be synthesized into hardware

## Slide 50: What is Synthesis ?
Synthesis = translation + optimization + Mapping
Phase II
Phase I

## Slide 51: Synthesizable Built-in Primitives
Multi-input Gates | Multi-output Gates | Tri-state Gates | Pull Gates | Unidirectional Switches | Bidirectional Switches
and nand or nor xor xnor | buf not | bufif0 bufif1 notif0 notif1 | pulldown pullup | cmos nmos pmos rcmos rnmos rpmos | rtran rtrainif0 rtranif1 tran tranif0 tranif1
Synthesizable !!
Non-Synthesizable !!

## Slide 52: Synthesizable Operator Types
Type of Operators | Symbols
Concatenate & replicate | { } {{ }}
Unary | ! ~ & ¦ ^
Arithmetic | * / % + - **
Logical shift | << >> <<< >>>
Relational | > < >= <=
Equality | == === != !==
Binary bit-wise | & ¦ ^ ~^
Binary logical | && ¦¦
conditional | ? :
DC allows “**” operator performs yx synthesis, but exponentiation is only supported if the base is a power of 2 (ex: 2x, 4x, 8x, …) or the exponent is 2 (ex: y2)

## Slide 53: Combinational Logic
initial value for combinational logic will be ignored for synthesis
No assign block (legal but not synthesizable)
WRONG!!!
logic a =0;
assign a=b+c;
Wrong

## Slide 54: How to Properly Initialize a DFF?
Reset DFF registers
  You can reset DFF when rst_n triggers
  Do not use initial begin since it is not synthesizable
always_ff@(posedge clk or negedge rst_n)
if(rst_n == 0)
a <= 0;
else
a <= b;
initial a = 0;
logic a = 0;
Bad for design, not synthesizable
Only for testbench simulation
Initial values are ignored for synthesis

## Slide 55: Combinational Loop
A variable cannot be assigned by itself in combinational logic
  Combinational loop (timing loop)
WRONG!!! Not synthesizable
Same variable in both sides
always_comb
a = b+a;
always_ff@(posedge clk)
a <= b+a;
Same variable in both sides
only allowed in seq. logic

## Slide 56: Resource Sharing: Area Reduction Technique
HDL coding style can force a specific topology to be synthesized
A B C
A
B
D A
B
E
SUM1
SUM2
SUM3
A
B C
D
E
SUM1
SUM2
SUM3
Sharing
SUM1 = A+B+C; SUM2 = A+B+D; SUM3 = A+B+E;
assign tmp = A+B; SUM1 = tmp +C; SUM2 = tmp +D; SUM3 = tmp +E;

## Slide 57: Architectural Techniques : Resource Sharing

## Slide 58: Coding Guidelines for Clocks (1/3)
Using single global clock (Fig. (a))
Avoiding mixed use of both positive and negative edge-triggered flip-flops (Fig. (b))
Avoiding using internally generated clock signals (Fig. (c))
Avoiding using gated clocks (in next slides)
Digital System Designs and Practices Using Verilog HDL and FPGAs John Wiley

## Slide 59: Coding Guidelines for Clocks (2/3)
Clock Gating
  For low power design
  50% - 70% power consumed in clock network report
  Doing the clock gating by using power synthesis tools
always @ (posedge clk)
if(en)
Q <= Q_nxt
assign clk1 = clk &en;
always @ (posedge clk1)
Q <= Q_nxt

## Slide 60: Coding Guidelines for Clocks (3/3)
always@(posedge clk)
if (en) Q <= D;
always@(posedge clk)
if (en) begin
for (i=0; i<8; i=i+1)
s[ i ] = a[ i ] & b[ i ];
end
always@(posedge clk)
Q <= (en)? D : Q;
always@(posedge clk)
case (en)
1’b1 : Q <= D;
1’b0 : Q <= Q;
endcase
high activity !!
low activity !!
CG cell
By Power compiler

## Slide 61: Partitioning for Synthesis (1/2)
Keep related logic within the same module
Register all outputs
Digital System Designs and Practices Using Verilog HDL and FPGAs John Wiley

## Slide 62: Partitioning for Synthesis (2/2)
Maintaining the original hierarchy
Digital System Designs and Practices Using Verilog HDL and FPGAs John Wiley

## Slide 63: Logic Grouping
A = B + C + D + F;
+
+
+
B
C
D
F
A
A = (B + C) + (D + F);
+
+
+
B
C
D
F
A

## Slide 64: Priority Encoder if-else (?:) v.s. case
module mux (in0, in1, in2, in3, sel, mux_out);
input in0, in1, in2, in3;
input [1:0] sel;
output mux_out;
reg mux_out;
always @(in0 or in1 or in2 or in3 or sel) begin
case (sel)
2'b00: mux_out = in0;
2'b01: mux_out = in1;
2'b10: mux_out = in2;
default:mux_out = in3;
endcase
end
endmodule
module p_encoder (in0, in1, in2, in3, sel, p_encoder_out);
input in0, in1, in2, in3;
input [1:0] sel;
output p_encoder_out;
reg p_encoder_out;
always @(in0 or in1 or in2 or in3 or sel) begin
if (sel == 2'b00)
p_encoder_out = in0;
else if (sel == 2'b01)
p_encoder_out = in1;
else if (sel == 2'b10)
p_encoder_out = in2;
else p_encoder_out = in3;
end
endmodule
in0
in1
in2
in3
mux_out
sel
in0
in1
in2
in3
sel=00
sel=01
sel=10
p_encoder_out
Generally, If-Else is slower unless you intend to build a priority encoder!
case will have faster ckt

## Slide 65: Priority Encoder “if-then-else” When to use?
Assign highest priority to a late arriving critical signal
Nested “if-then-else” can increase area and delay
Use “case” statement if possible to describe the same function
in [4]
in [3]
S
S
S
S
in [2]
in [1]
in [0]
always_comb
begin
if (sel == 3'h0)
out = in[0];
else if (sel == 3'h1)
out = in[1];
else if (sel == 3'h2)
out = in[2];
else if (sel == 3'h3)
out = in[3];
else if (sel == 3'h4)
out = in[4];
else
out = in[5];
end
Put the slowest input close to the output

## Slide 66: Inefficient vs. Efficient Description
module count ( clock, reset, and_bits, or_bits, xor_bits);
input clock, reset;
output and_bits, or_bits, xor_bits;
reg and_bits, or_bits, xor_bits;
reg [2:0] count;
always @ (posedge clock) begin
if (reset)
count = 0;
else
begin
count = count + 1;
and_bits = &count;
or_bits = |count;
xor_bits = ^count;
end
end
endmodule
Six inferred registers
Separate combinational and sequential circuits
always @ (posedge clock)
begin
if (reset)
count = 0;
else
count = count + 1;
end
always @ (count)
begin // combinational circuits
and_bits = &count;
or_bits = |count;
xor_bits = ^count;
end
Three registers are inferred

## Slide 67: References
Verilog HDL – Samir Palnitkar
The Fundamentals of Efficient Synthesizable Finite State Machine Design using NC-Verilog and Build Gates – Clifford E. Cummings
Verilog: Frequently Asked Questions: Language, Applications and Extensions - Shivakumar S. Chonnad, Needamangalam B. Balachander

## Slide 68: References for SystemVerilog
Books
  SystemVerilog for Verification: A Guide to Learning the Testbench Language Features by Chris Spear (Hardcover - Jul 10, 2006)
  SystemVerilog for Design: A Guide to Using SystemVerilog for Hardware Design and Modeling by Stuart Sutherland, Simon Davidmann, Peter Flake, and P. Moorby (Hardcover - Jul 20, 2006)
Web site
  Official site: www.systemverilog.org
  On-line tutorial: http://www.doulos.com/knowhow/sysverilog/
Course
  MIT 6.375 Complex Digital Systems

## Slide 69: Reference
https://hom-wang.gitbooks.io/verilog-hdl/content/
http://www.asic-world.com/verilog/index.html
https://www.slideshare.net/itembedded/verilog-14596615
http://www.sunburst-design.com/papers/CummingsSNUG1999SJ_SynthMismatch.pdf
http://www-inst.eecs.berkeley.edu/~cs150/fa13/agenda/
http://www.ee.ic.ac.uk/pcheung/teaching/ee2_digital/
Notes: http://referencedesigner.com/tutorials/verilog/verilog_01.php

## Slide 70: Note.由C語言學習Verilog的思維轉換
軟體是循序的，而硬體是並行的
硬體要循序，要靠clock和FSM
  靠clock並且搭配FSM，當一個state完成後，進入下一個state，這樣就能依照clock的進行，而達成循序的要求
Verilog程式碼沒有先後之分
  blocking assignment有先後執行順序，而nonblocking assignment同時執行
硬體『描述』語言，而非硬體『程式』語言
  先寫的不代表先執行，後寫的也不代表後執行，只是代表硬體的架構的描述，也就是說，將原來的電路圖，變成文字描述而已
Notes: https://www.cnblogs.com/oomusou/archive/2008/06/17/c_verilog_mental_thinking.html

## Slide 71: Verilog vs C
Verilog 有些語法像C ，但不是軟體語言
  No pointer, no return function, no recursive calls, no memory allocation
Verilog  Hardware module
  了解每一行Verilog code 會產生的硬體架構
  知道想做的硬體架構應該對應的Verilog code 寫法 (Coding style)
何時可以用很像C的高階寫法
  在 testbench 時使用

## Slide 72: 幫幫EDA tools: Helping the Tools* 為什麼要建議某種寫法?
In an ideal world it shouldn’t matter how you write the Verilog – optimization in the CAD tools will find the best solution. But the world is not ideal (yet…)
Tools work best on smaller problems
  Need to partition real problem into pieces for you and the tools (it’s hard to think about 1M gates at one time). Decompose large problems into smaller problems and then connect the solutions
  Hierarchy in Verilog " partitions in physical layout
Tools use your code as a starting point.
  Your structure isn’t completed eliminated (this is good…)
  Little optimization will be done between top-level blocks
Structure of the problem is often important
  Finding a “good” way to think about the problem is key
Like optimizing compilers for C, tools are good for local optimizations but don’t expect them to rewrite your code and change your algorithm. With practice you’ll learn what works and what doesn’t…
*adapted from a Stanford EE271 lecture by Mark Horowitz
請用不讓Tool誤解的寫法
Notes: Architecture to Verilog An Extended Example

## Slide 73: Simulation and Synthesis
Not all of the Verilog commands can be synthesized into hardware
Our primary interest is to build hardware, we will emphasize a synthesizable subset of the language
Will divide HDL code into synthesizable modules and a test bench (simulation).
  The synthesizable modules describe the hardware.
  The test bench checks whether the output results are correct (only for simulation and cannot be synthesized)
testbench.v
pattern.v
design.v
(synthesizable)

## Slide 74: From Spec to Verilog RTL: TIPS for HW
Read the spec
Create some patterns to make sure you understand spec
  Try some boundary cases
Draw the dataflow
Create your block diagram (architecture)
  Try the naïve method first
  Any possible optimization?
    You can skip simple logic minimization. EDA tools will do that for you.
  Possible properties to use: constant/repeat behaviour/decomposition
Based on architecture, find the related Verilog code