## Slide 1: Digital Circuits and Systems Lecture 4 Modeling Combinational Logic
Tian Sheuan Chang

## Slide 2: System view

## Slide 3: A12
https://www.phonearena.com/news/Apples-A12-chip-packed-with-70-percent-more-transistors_id109291
https://www.loveios.net/2018/08/tsmc-virus-attack-may-affect-a12-production.html

## Slide 5: System on a Chip (SOC)
Source: ARM
Notes: Many systems include Analog and Digital functions.
This course will deal only with digital designs.

## Slide 6: PYNQ

## Slide 7: Breakdown of Modern SOC Design
Core
  CPU/DSPs/GPUs
  Hardware accelerators (AI engine/video codec/MP3 codec)
  Complex data path + FSMs (pipeline/parallel)
Bus
  Connect core and peripherals
  MUX/arbiters
Peripheral
  Interface from/to the external
  speech/audio, camera/display, I2S/I2C, GPIO
  Serial to parallel, parallel to serial + FSM

## Slide 8: An Example AMBA System

## Slide 9: From C Array to Memory Access
http://www.phatcode.net/res/260/files/html/SystemOrganizationa2.html
Memory Write Operation
Memory Read Operation
CPU = Memory [125]
Memory [125] = 0

## Slide 10: How CPU access these I/O interface?
Memory mapped I/O (treat other components as memory)
Notes: https://www.chegg.com/homework-help/questions-and-answers/exercise-828-use-mips-memory-mapped-o-interact-user-time-user-presses-button-pattern-choic-q30535077
http://vegetableavenger.blogspot.com/2013/12/beagleboen-black-io-library-mmap.html

## Slide 11: Example: USB sub system memory map in Beagle board
I/O與memory共用記憶體空間，不用特別的指令來存取I/O，以記憶體讀寫的方式來進行I/O port的存取，在本文中使用的是ARM的核心，TI AM335X，便提供這種方式來進行I/O port的存取。
透過 memory mapped I/O的方式，許多外接元件或是module，都可以透過memory access的方式來進行存取，從C語言的角度來看，則是只需要用指標就可以存取這些記憶體，只要知道mapped的範圍，便可以存取裝置，在使用上非常直覺。
Notes: http://vegetableavenger.blogspot.com/2013/12/beagleboen-black-io-library-mmap.html

## Slide 12: AHB-Lite
mux

## Slide 13: AHB Interconnect
Basic components:
Master
Slave
Arbiter
Decoder
Mux

## Slide 14: Outline
From K-Map to Verilog [Dally 7.1]
Combinational building blocks – the idioms of digital design [Dally 8]
  Decoder (binary to one-hot)
  Encoder (one-hot to binary)
  Muliplexer (select one of N)
  Arbiter (pick first of N, 找第一個1 ) and priority encoder
  Comparators
  Read-only memories (ROM) / random access memory (RAM)

## Slide 15: 學習重點
知道如何對應基本硬體與Verilog code
  寫法很多種，哪一個比較好?
  Verilog語法的差別
從2-bit 到 16bit 怎麼設計?怎麼寫?
  Iterative circuit
  Behavior level Verilog

## Slide 16: From K-map to Verilog 從手動化簡到自動化電路 case/casez/casex

## Slide 17: Prime Number Detection
F(d,c,b,a) is true if input d,c,b,a is prime
Schematic Logic Diagram:

## Slide 18: Karnaugh Map of 4-bit Prime Number
a
Position of minterms on a 4-bit Karnaugh map
0
1
3
2
4
5
7
6
ba
12
13
15
14
8
9
11
10
00
01
11
10
00
01
11
10
d
b
c
dc
00
01
11
10
a
b
c
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
001X
X101
0XX1
00
01
11
10
X011
NAND for CMOS

## Slide 19: 更進一步化簡 Decimal Prime: includes don’t cares
00
01
11
10
00
01
11
10
a
b
c
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
11
10
01
11
a
b
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
X1X1
00
01
11
10
X01X
0XX1
XX11
c
Cover:
0XX1
X01X
f = (a d) V (b c)
V
V
¯
¯

## Slide 20: 4-bit Prime Number Function in Verilog Code – Using case
You can have a simplified Verilog coding if with don’t care input
這很好，可是若有DON’T CARE INPUT，寫法可以更化簡
module prime(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
logic isprime ;
always_comb begin
case(in)
1,2,3,5,7,11,13: isprime = 1'b1 ;
default: isprime = 1'b0 ;
endcase
end
endmodule

## Slide 21: 4-bit Prime Number Function in Verilog Code – Using casez
http://www.sunburst-design.com/papers/CummingsSNUG1999SJ_SynthMismatch.pdf
http://www.cnblogs.com/poiu-elab/archive/2012/11/02/2751323.html
 | case | casez | casex
比對的值 | 0, 1, Z. X | 0, 1, X | 0, 1
當作do’t care |  | Z | X, Z
電路合成 | 0, 1 | 0, 1 | 0, 1
使用casez 利用到DON’T CARE INPUT，
但避免X propagation，造成
Simulation-synthesis mismatch
X: unknown, Z: high impedence, ?: Z
當輸入有X，以下電路
會全部X
module prime1(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
logic isprime ;
always_comb begin
casez(in)
4'b0??1: isprime = 1 ;
4'b001?: isprime = 1 ;
4'b?011: isprime = 1 ;
4'b?101: isprime = 1 ;
default: isprime = 0 ;
endcase
end
endmodule
Priority encoder
Notes: http://www.sunburst-design.com/papers/CummingsSNUG1999SJ_SynthMismatch.pdf
http://www.cnblogs.com/poiu-elab/archive/2012/11/02/2751323.html
1、我們在寫代碼的時候如果用了case，那麼就不要在index列表裡面出現x/z/?，綜合工具認不出這些，都會當做don't care
2、casez和casex綜合的結果是一致的。
3、casez稍好用一些，因為它可以用來代表don't care的值
4、最重要的一點就是，casez和casex其實沒有孰優孰劣

## Slide 22: 4-bit Prime Number Function in Verilog Code – Using assign
簡單的化簡就留給EDA tools 做
複雜的架構才值得花時間
You don’t need to simplify logic
by yourself, Left this to EDA tools
module prime(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
wire isprime = (in[0] & ~in[3]) |
(in[1] & ~in[2] & ~in[3]) |
(in[0] & ~in[1] & in[2]) |
(in[0] & in[1] & ~in[2]) ;
endmodule

## Slide 23: 4-bit Prime Number Function in Verilog Code – Result of synthesizing description using case
Quiz:
Where are these gates?
identify the critical path?
module prime ( in, isprime );
input [3:0] in;
output isprime;
wire n1, n2, n3, n4;
OAI13 U1 ( .A1(n2), .B1(n1), .B2(in[2]), .B3(in[3]), .Y(isprime) );
INV U2 ( .A(in[1]), .Y(n1) );
INV U3 ( .A(in[3]), .Y(n3) );
XOR2 U4 ( .A(in[2]), .B(in[1]), .Y(n4) );
OAI12 U5 ( .A1(in[0]), .B1(n3), .B2(n4), .Y(n2) );
endmodule

## Slide 24: Synthesis Reports
****************************************
Report : area
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Library(s) Used:
XXXXX
Number of ports: 5
Number of nets: 9
Number of cells: 5
Number of references: 4
Combinational area: 7.000000
Noncombinational area: 0.000000
Net Interconnect area: undefined (Wire load has zero net area)
Total cell area: 7.000000
Total area: undefined
****************************************
Report : timing
-path full
-delay max
-max_paths 1
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Operating Conditions:
Wire Load Model Mode: enclosed
Startpoint: in[2] (input port)
Endpoint: isprime (output port)
Path Group: (none)
Path Type: max
Des/Clust/Port Wire Load Model Library
------------------------------------------------
prime 2K_5LM XXXXX
Point Incr Path
-----------------------------------------------------------
input external delay 0.000 0.000 r
in[2] (in) 0.000 0.000 r
U4/Y (EX210) 0.191 0.191 f
U5/Y (BF051) 0.116 0.307 r
U1/Y (BF052) 0.168 0.475 f
isprime (out) 0.000 0.475 f
data arrival time 0.475
-----------------------------------------------------------
(Path is unconstrained)
Left part: area report
Right part: timing report

## Slide 25: Constraint File
//設定clock, I/O 限制
create_clock "clk" -name clk -period 2 -waveform {0 1.7}
set_clock_uncertainty 0.2 clk
set_fix_hold all_clocks()
set_input_delay 0.5 -clock clk {in}
set_output_delay -max 0.8 -clock clk {isprime}
//設定 loading
set_load -pin_load 5 {isprime}
//Note: these commands are for practical applications to include
// clock jitter, input/output loading capacitances

## Slide 26: Test bench
//this test module is included to
//simulate the behavior of your
//Verilog-HDL description
//Note: very often input data
//will be limited
Quiz: Why “divide-and-conquer”
Is often exploited in DCS design?
module test_prime ;
reg [3:0] in ;
wire isprime ;
// instantiate module to test
prime p0(in, isprime) ;
initial begin
in = 0 ;
repeat (16) begin
#100
$display("in = %2d isprime = %1b",in,isprime) ;
in = in+1 ;
end
end
endmodule

## Slide 27
# in = 0 isprime = 0
# in = 1 isprime = 1
# in = 2 isprime = 1
# in = 3 isprime = 1
# in = 4 isprime = 0
# in = 5 isprime = 1
# in = 6 isprime = 0
# in = 7 isprime = 1
# in = 8 isprime = 0
# in = 9 isprime = 0
# in = 10 isprime = 0
# in = 11 isprime = 1
# in = 12 isprime = 0
# in = 13 isprime = 1
# in = 14 isprime = 0
# in = 15 isprime = 0
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 28: Summary
K-Map helps you understand how logic synthesizer works
  But no need to do it by yourself
  Synthesis tool will do the optimization
Use case
Or casez if you have don’t care input

## Slide 29: Decoder and encoder (binary <-> one hot)
mux

## Slide 30: Binary to One-Hot Representation (Decoder)
Binary One-hot
000 00000001
001 00000010
010 00000100
… …
110 01000000
111 10000000
Binary input a to one-hot output b
b[i] = 1 if a = i
b = 1<<a
n
m
a
n
m
2
≤
b
Decoder
*can be found in source and communication systems
常用於記憶體的address decoder
Used in address decoder for memory
Notes: 兩種寫法
Behaviour level b[i] = 1 if a = I
2. Syntheziable b = 1<<a

## Slide 31: Verilog implementation of a decoder
// a - binary input (n bits wide)
// b - one hot output (m bits wide)
module dec(a, b) ;
parameter n=2 ;
parameter m=4 ;
input [n-1:0] a ;
output [m-1:0] b ;
wire [m-1:0] b;
assign b = 1<<a ;
endmodule
n
m
a
n
m
2
≤
b
Decoder
//this is a parameterized design
//you need to assign parameters
//when exploited.

## Slide 32: From 2->4 decoder to 6->64 Decoder 大的Decoder 如何又快又省
Need hierarchical design 階層式設計
6->64 decoder requires:
  64 6-input AND gates (384 inputs)
6->64 decoder using 2->4 decoders requires:
  12 2-input AND gates (24 inputs)
  64 3-input AND gates (192 inputs)
Faster, smaller, lower power performances can be achieved.
Notes: 先講結論

## Slide 33: 2-Stage decoders – the picture

## Slide 34: Encoder
a3 | a2 | a1 | a0 | b1 | b0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
a 4 -> 2 encoder
a
3
a
1
a
2
a
0
b
1
b
0
那大的Encoder呢? E.g. 16-> 4

## Slide 35: 16->4 Encoder
a
[
1
5
:
1
2
]
4
a
[
1
1
:
8
]
4
a
[
7
:
4
]
4
a
[
3
:
0
]
4
2
2
2
2
b
[
1
:
0
]
b
[
3
:
2
]
2
2
4:2
4:2
4:2
4:2
4:2
High bits
Low bits
One hot
Quiz: how to achieve
This structure?
//for 2 MSB’s
//for 2 LSB’s

## Slide 36: Two writing styles 兩種寫法
// encoder - fixed width
module Enc42a(a, b) ;
input [3:0] a ;
output [1:0] b ;
wire [1:0] b ;
assign b[1] = a[3] | a[2] ;
assign b[0] = a[3] | a[1] ;
endmodule
// encoder - fixed width
module Enc42a(a, b) ;
input [3:0] a ;
output [1:0] b ;
wire [1:0] b ;
always_comb begin
case (a)
4'b0001: b = 2'd0;
4'b0010: b = 2'd1;
4'b0100: b = 2'd2;
4'b1000: b = 2'd3;
4'b0000: b = 2'd0; // to faciltate large encoder
default: b = 2'dxx;
endcase
end
endmodule
Behavior level
More like schematic
Vote
To avoid simulation and synthesis mismatch,
Set default value to one of the options. E.g. b = 2’d0;
Notes: 建議使用behavior level寫法
好看易懂
幫助debug illegal input
可讓synthesizer 自己化簡

## Slide 37: Binary Encoder
Input is 1-hot
// Simple binary encoder (input is 1-hot)
module encode (A, Y);
input [7:0] A; // 8-bit input vector
output [2:0] Y; // 3-bit encoded output
reg [2:0] Y; // target of assignment
always @(A)
case (A)
8’b00000001: Y = 0;
8’b00000010: Y = 1;
8’b00000100: Y = 2;
8’b00001000: Y = 3;
8’b00010000: Y = 4;
8’b00100000: Y = 5;
8’b01000000: Y = 6;
8’b10000000: Y = 7;
default: Y = 3’bXXX; // Don’t care when input is not 1-hot
endcase
endmodule

## Slide 38
Cases are executed sequentially
// Priority encoder
module encode (A, Y);
input [7:0] A; // 8-bit input vector
output [2:0] Y; // 3-bit encoded output
reg [2:0] Y; // target of assignment
always @(A)
case (1’b1)
A[0]: Y = 0;
A[1]: Y = 1;
A[2]: Y = 2;
A[3]: Y = 3;
A[4]: Y = 4;
A[5]: Y = 5;
A[6]: Y = 6;
A[7]: Y = 7;
default: Y = 3’bXXX;// Don’t care when input is all 0’s
endcase
endmodule

## Slide 39: multiplexer
mux

## Slide 40: Multiplexer (one-hot selection signals)
Multiplexer:
  n k-bit inputs
  n-bit one-hot select signal s
  Multiplexers are commonly used as data selectors
Selects one of n k-bit inputs
s must be one-hot
b=a[i] if s [i] = 1

## Slide 41: 兩種架構，哪個好?
AND-OR structure
Tri-state structure
Quiz: What’s the difference between these two implementations?

## Slide 42: MUX4 v.s. MUX3
Behavior level
More like schematic
Vote
module mux3a(a2, a1, a0, s, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2 ; // inputs
input [2:0] s ; // one-hot select
output[k-1:0] b ;
logic [k-1:0] b ;
always_comb begin
case(s)
3'b001: b = a0 ;
3'b010: b = a1 ;
3'b100: b = a2 ;
default: b = {k{1'bx}} ;//don’t care “X”
endcase
end
endmodule
Mux4(a3, a2, a1, a0, s, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2, a3 ;
input [3:0] s ; // one-hot select
output[k-1:0] b ;
wire [k-1:0] b = ({k{s[0]}} & a0) |
({k{s[1]}} & a1) |
({k{s[2]}} & a2) |
({k{s[3]}} & a3) ;
endmodule
Notes: 建議使用behavior level寫法
好看易懂
幫助debug illegal input
可讓synthesizer 自己化簡

## Slide 43: Binary Select MUX

## Slide 44: 兩種寫法
// 3:1 multiplexer with binary select (arbitrary width)
module Muxb3(a2, a1, a0, sb, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2 ; // inputs
input [1:0] sb ; // binary select
output[k-1:0] b ;
wire [2:0] s ;
dec #(2,3) d(sb,s) ; // Decoder converts binary to one-hot
mux3 #(k) m(a2, a1, a0, s, b) ; // multiplexer selects input
endmodule
always_comb begin
case(sb)
0: b = a0;
1: b = a1;
2: b = a2;
default: b = {k{1'bx}};
end
那大的MUX怎麼辦?
Notes: Common design error
With available one-hot select signals, convert it to binary, and apply binary select
No need to do this. Just use one-hot select signals

## Slide 45: Arbiter and priority encoder 找第一個1 000010111

## Slide 46: Arbiter
Arbiter handles requests from multiple devices to use a single resource
  For bus arbitration
  Normalization in floating point operations
n
n
Finds first “1” bit in r
g[i]=1 if r[i]=1 and r[j]=0 for j>i
Arbiter
r
g
e.g. LSB has the higher priority
input 0101_1100
Output 0000_0100
Leading one detector

## Slide 47: 1-Bit and 4-bit Arbiters
//initial value=1
//as a leaf cell
Using Bit-Cell
Using Look-Ahead
Iterative circuit
Quiz: What’s the difference between
These two?
g[i]=1 if r[i]=1 and r[j]=0 for j>i
目前req
更高權限的req
G0=r0,
G1=none & r1 = r0’ & r1;
更高權限的req
目前req
Notes: Linear chain has longer delay
Expand it with look ahead for shorter delay
G0=r0,
G1=none & r1 = r0’ & r1;
G2 =

## Slide 48: Implementing Arbitrary Width Arbiter Using Verilog
// arbiter (arbitrary width),
// LSB is the highest priority
module Arb(r, g) ;
parameter n=8 ;
input [n-1:0] r ;
output [n-1:0] g ;
wire [n-1:0] c ;
wire [n-1:0] g ;
assign c = {(~r[n-2:0] & c[n-2:0]),1'b1} ;
assign g = r & c ;
endmodule
Bit-slice coding style using
concatenation {a, b}
index ranges c[n-2:0]
c is 1s up to first 1 in r, then 0s
always_comb begin
casez(r)
4'b0000: g = 4'b0000;
4'b???1: g = 4'b0001;
4'b??10: g = 4'b0010;
4'b?100: g = 4'b0100;
4'b1000: g = 4'b1000;
default: g = 4'hx;
endcase
end
g[i]=1 if r[i]=1 and r[j]=0 for j>i
c
Notes: 看起來像循環，其實不然，因為每個c的bit都只和他自己小一位元的bit有關

## Slide 49: Priority Encoder
Priority Encoder:
  n-bit input signal a
  m-bit output signal b
    b indicates the position of the first 1 bit in a
always_comb begin
casez(r)
4'b???1: g = 2'd0;
4'b??10: g = 2'd1;
4'b?100: g = 2'd2;
4'b1000: g = 2'd3;
default: g = 2'dx;
endcase
end
Check example 8.3 for programmable priority encoder
Notes: Note. Outputs x, not 0, in the case where the input = 0

## Slide 50: Priority Encoder with if-else
assign valid_in = |in; //檢查不合法輸入
always @(in) begin
if (in[3]) y = 3; else
if (in[2]) y = 2; else
if (in[1]) y = 1; else
if (in[0]) y = 0; else
y = 2'bx;
end

## Slide 51
module pri_encoder_using_if (
output reg [1:0] binary_out , // 2 bit binary output
input wire [3:0] encoder_in , // 4-bit input
input wire enable // Enable for the encoder
);
//--------------Code Starts Here-----------------------
always_comb
begin
binary_out = 0;
if (enable) begin
if (encoder_in[0] == 1) begin
binary_out = 1;
end else if (encoder_in[1] == 1) begin
binary_out = 2;
end else if (encoder_in[2] == 1}) begin
binary_out = 3;
end
end
endmodule

## Slide 52: Priority Encoder with Priority if-else (Optional)
Priority (SystemVerilog syntax)
  告訴simulator/synthesizer 就照這個順序執行，沒列在上面的就當作don’t care，可以被化簡
module encoder (
input in0 , in1 , in2 , in3 ,
output logic [3:0] encoded_output ;
always_comb
priority if ( in0 ) encoded_output = 4’b0001 ;
else if ( in1 ) encoded_output = 4’b0010 ;
else if ( in2 ) encoded_output = 4’b0100 ;
else if ( in3 ) encoded_output = 4’b1000 ;
endmodule
http://www.sutherland-hdl.com/papers/2005-SNUG-paper_SystemVerilog_unique_and_priority.pdf
Notes: http://www.sutherland-hdl.com/papers/2005-SNUG-paper_SystemVerilog_unique_and_priority.pdf

## Slide 53: Priority Encoder if-else (?:) v.s. case
module mux (in0, in1, in2, in3, sel, mux_out);
input in0, in1, in2, in3;
input [1:0] sel;
output mux_out;
reg mux_out;
always @(in0 or in1 or in2 or in3 or sel) begin
case (sel)
2'b00: mux_out = in0;
2'b01: mux_out = in1;
2'b10: mux_out = in2;
default:mux_out = in3;
endcase
end
endmodule
module p_encoder (in0, in1, in2, in3, sel, p_encoder_out);
input in0, in1, in2, in3;
input [1:0] sel;
output p_encoder_out;
reg p_encoder_out;
always @(in0 or in1 or in2 or in3 or sel) begin
if (sel == 2'b00)
p_encoder_out = in0;
else if (sel == 2'b01)
p_encoder_out = in1;
else if (sel == 2'b10)
p_encoder_out = in2;
else p_encoder_out = in3;
end
endmodule
in0
in1
in2
in3
mux_out
sel
in0
in1
in2
in3
sel=00
sel=01
sel=10
p_encoder_out
Generally, If-Else is slower unless you intend to build a priority encoder!
case 合成的電路比較快

## Slide 54: Priority Encoder “if-then-else” When to use?
Assign highest priority to a late arriving critical signal
Nested “if-then-else” can increase area and delay
Use “case” statement if possible to describe the same function
in [4]
in [3]
S
S
S
S
in [2]
in [1]
in [0]
always_comb
begin
if (sel == 3'h0)
out = in[0];
else if (sel == 3'h1)
out = in[1];
else if (sel == 3'h2)
out = in[2];
else if (sel == 3'h3)
out = in[3];
else if (sel == 3'h4)
out = in[4];
else
out = in[5];
end
最慢到的輸入放在最靠近輸出

## Slide 55: TLDR: if-then-else vs. case
If-then-else often infers a cascaded encoder
  inputs signals with different arrival time
case infers a single-level mux
  case is better if priority encoding is not required
  case is generally simulated faster than if-then-else
conditional assignment (? :)
  infers a mux with slower simulation performance
  better avoided

## Slide 56: comparators

## Slide 57: Magnitude Comparator
a
n
b
n
Magnitude
Comparator
gt
//bit-slice design with leaf cell (from LSB)
//note that initial value to be considered
// magnitude comparator
module MagComp(a, b, gt) ;
parameter k=8 ;
input [k-1:0] a, b ;
output gt ;
wire [k-1:0] eqi = a ~^ b ;
wire [k-1:0] gti = a & ~b ;
wire [k:0] gtb {((eqi[k-1:0] & gtb[k-1:0]) | gti[k-1:0]), 1’b0} ;
wire gt = gtb[k] ;//MSB is selected as output gt;
endmodule
assign gt = (a > b) ;

## Slide 58: Modeling Memories

## Slide 59: Modeling Memories
Objectives
Learn how to model memories with Verilog.
Learn how to model a bidirectional port in Verilog.

## Slide 60: Modeling a Memory Device
A memory device must do two things:
Declare a memory of appropriate size.
  reg [MSB : LSB] <memory_name> [first_addr : last_addr];
  Ex: reg [3:0] mem [0:15]; // 4 bits, 16 words
Provide some level of access to its contents, such as:
  Read only
  Read and write
  Write and simultaneous read
  Multiple reads, simultaneous to a single write
  Multiple simultaneous reads and writes, with some method of ensuring consistency

## Slide 61: Memory Addressing
A memory element is addressed by the index to the memory array. You can only reference one word of memory at a time.
  module mems;
  reg [8:1] mema [0:255]; // declare memory called mema
  reg [8:1] mem_word; // temp register called mem_word
  ...
  initial begin
  //Display contents of the 6th memory address
  $displayb (mema[5]);
  //Display the MSB of the 6th memory word
  mem_word = mema[5];
  $displayb (mem_word[8]);
  end
  endmodule

## Slide 62: Loading a Memory Device
You can load a ROM or RAM with data by using a $readmem task
Assign values to each word of the memory array in a loop.
  for (i=0; i < memsize; i = i+1) // initialize memory
  mema[i] = {wordsize{1'b1}};
Call to the $readmem system task.
  // load memory data from a file
  $readmemb("mem_file.txt", mema);

## Slide 63: Modeling a Simple ROM
The data for the ROM is stored in a separate file
myrom.v
  `timescale 1ns/10ps
  module myrom (read_data, addr, read_en_);
  input read_en_;
  input [3:0] addr;
  output [3:0] read_data;
  reg [3:0] read_data;
  reg [3:0] mem [0:15]; // 4 bits, 16 words
  initial
  $readmemb (“my_rom_data”, mem); (參考前面投影片)
  always @(addr or read_en_)
  if (!read_en_)
  read_data = mem[addr];
  endmodule
my_rom_data
  0000
  0101
  1100
  0011
  1101
  0010
  0011
  1111
  1000
  1001
  1000
  0001
  1101
  1010
  0001
  1101

## Slide 64: Modeling a Simple RAM
RAM models are slightly more complicated than ROM models because there must be both read and write capability, usually with the same data bus. This requirement necessitates a new modeling technique to handle the bidirectional buses
Modeling 256*16 Memory
  module mem_model (data_bus, addr, oeb, web);
  inout [15:0] databus;
  input [ 7:0] addr;
  input oeb, web;
  reg [15:0] mem [0:255];
  assign databus = (~oeb) ? mem [addr] : 16’bz;
  always@(negedge web)
  mem [addr] <= databus;
  endmodule

## Slide 65: Using Bidirectional Ports
You declare bidirectional ports with the inout keyword.
  inout [7:0] databus;
Bidirectional ports follow these rules:
An inout port cannot be declared as a register, it is always a net.
  So the simulator can determine the resulting value of multiple drivers.
Your design should drive an inout port from only one direction at a time.
  For example, if you drive write data onto the bidirectional data bus of a RAM model while you are using the bus to read RAM data, a logic conflict may result, causing the bus to become unknown.
  You must design logic around the inout port to ensure proper operation.

## Slide 66: Read only memories (ROM) Random access Memory (RAM)
More examples

## Slide 67: Read-only memory (ROM)
存常數值，
可實現任意函數
需要address decoder，所以大小夠大才划算
d[m] = ROM[a[n]];
address
2n word lines
m bit lines

## Slide 68
2-D array implementation
(c) 2005-2012 W. J. Dally
Row selector
Column selector

## Slide 69: ROM Model: loading data from file
module rom_using_file (
input wire [7:0] address , // Address input
output wire [7:0] data , // Data output
input wire read_en , // Read Enable
input wire ce // Chip Enable
);
reg [7:0] mem [0:255] ;
assign data = (ce && read_en) ? mem[address] : 8'b0;
initial begin
$readmemb("memory.list", mem); // memory_list is memory file
end
endmodule
http://www.asic-world.com/code/sv_examples/rom_using_file.sv
11001
11010
@5 11001000 // 将11001存入mem[5]
@2 11010000 //将11010存入mem[2]
@7 //直至7开始
11001000
00000000
111111111
memory.list
適合大的ROM size
Notes: http://www.asic-world.com/code/sv_examples/rom_using_file.sv

## Slide 70: ROM with case
module rom_using_case (
input wire [7:0] address , // Address input
output reg [7:0] data , // Data output
input wire read_en , // Read Enable
input wire ce // Chip Enable
);
always_comb
begin
case (address)
0 : data = 10;
1 : data = 55;
2 : data = 244;
3 : data = 0;
4 : data = 1;
……
13 : data = 8'h90;
14 : data = 8'h70;
15 : data = 8'h90;
endcase
end
endmodule
http://www.asic-world.com/code/sv_examples/rom_using_case.sv
適合很小的ROM size
Notes: http://www.asic-world.com/code/sv_examples/rom_using_case.sv

## Slide 71: RAM Model
module ram_sp_sr_sw #(parameter DATA_WIDTH = 8,
parameter ADDR_WIDTH = 8,
parameter RAM_DEPTH = (1 << ADDR_WIDTH))(
input wire clk , // Clock Input
input wire [ADDR_WIDTH-1:0] address , // Address Input
inout wire [DATA_WIDTH-1:0] data , // Data bi-directional
input wire cs , // Chip Select
input wire we , // Write Enable/Read Enable
input wire oe // Output Enable
);
//--------------Internal variables----------------
reg [DATA_WIDTH-1:0] data_out ;
// Use Associative array to save memory footprint
typedef reg [ADDR_WIDTH-1:0] mem_addr;
reg [DATA_WIDTH-1:0] mem [mem_addr];
http://www.asic-world.com/code/sv_examples/ram_sp_sr_sw.sv
Notes: http://www.asic-world.com/code/sv_examples/ram_sp_sr_sw.sv

## Slide 72
//--------------Code Starts Here------------------
// Tri-State Buffer control
// output : When we = 0, oe = 1, cs = 1
assign data = (cs && oe && !we) ? data_out : 8'bz;
// Memory Write Block
// Write Operation : When we = 1, cs = 1
always @ (posedge clk)
begin : MEM_WRITE
if ( cs && we ) begin
mem[address] = data;
end
end
// Memory Read Block
// Read Operation : When we = 0, oe = 1, cs = 1
always @ (posedge clk)
begin : MEM_READ
if (cs && !we && oe) begin
data_out = mem[address];
end
end
endmodule // End of Module ram_sp_sr_sw

## Slide 73: Reference
[Dally] Ch. 7. 8. 9
[Roth] Ch. 4
http://www.asic-world.com/index.html