## Slide 1: Lecture 5 Timing
Tian Sheuan Chang

## Slide 2: Outlines
Timing definition
How to read a timing report

## Slide 3: Some defintions

## Slide 4: Edge-Triggered D Flip Flop
Setup time: inputs become stable before rising clock;
Hold time: inputs remain stable after rising clock;
Setup time
Hold time
Notes: 輸入在activate clock edge 前後不能變動的時間

## Slide 5: How Fast My Design Can Run?
Up to 100MHz? 200MHz?
Slower at 10KHz, 20KHz? Any speed?

## Slide 6: How Fast My Design Can Run?
Fastest clock cycle time: Tc
Notes: What we care
  系統最快可以跑多快?Tc
  組合邏輯可以有的最長計算時間, Tpd

## Slide 7: Max Delay
  Tc >= tpcq + tpd + tsetup
  tpd <=Tc – (tpcq + tsetup )
Register overhead
If delay of comb. Logic is too long)
Setup time violation
DFF will catch the wrong value
1. clock run slower
Tc become larger
2. comb. Logic faster
Tpd smaller by pipeline or algorithm change
Notes: Example
10 1 10 1

## Slide 8: Min-Delay: Flip-Flops
If not hold,
(comb. Logic delay is too short)
hold time violation
DFF will catch the wrong value
1. Decreasing clock rate does not work
2. Increase tcd (e.g. add delay, buffer)
Notes: 如果不等式不成立，
(comb. Logic 的delay太短)
hold time violation
DFF值會不對
怎麼降clock速度都沒用
增加tcd (e.g. 加delay, buffer)
20141117 DIC
For example, a pipeline can use back-to-back registers
to sequence along an instruction opcode without modifying it. However, if the hold
time is large and the contamination delay is small, data can incorrectly propagate through
two successive elements on one clock edge, corrupting the state of the system. This is
called a race condition, hold-time failure, or min-delay failure. It can only be fixed by redesigning
the logic, not by slowing the clock. Therefore, designers should be very conservative
in avoiding such failures because modifying and refabricating a chip is catastrophically
expensive and time-consuming.

## Slide 9: Timing Paths
Input to register, register to register, register to output
  Start from or end to DFFs
Input to output
http://www.vlsi-expert.com/2011/03/static-timing-analysis-sta-basic-timing.html
Input to register
register to register
register to output
Input to output
3
5
2
7
Notes: http://www.vlsi-expert.com/2011/03/static-timing-analysis-sta-basic-timing.html

## Slide 12
https://sites.google.com/site/kennethnote/technology-detail/sta-timing

## Slide 13: Example
tdCQ = tcCQ = ts = 150ps
th = 250ps
tdMax = 850ps
tcMin = 100ps
Is hold time constraint met?
250ps <= 100+ 150ps
What is the minimum cycle time?
tcy >= 1150ps
Notes: 250<=150+100 met
Minimum cycle time 150+850+150 = 1150

## Slide 15: Add Clock Skew tk
Clock skew: arrival time of clock signal difference
Skew always reduces slack (margin)
Cycle get larger
Hold time tighter
check timing path as in timing report
Notes: Skew + => 後面DFF 的clock 到達時間比較晚

## Slide 16
Setup time check
Maximum Delay along the data path.
Minimum Delay along the clock path.
Delay in Data path
= max(wire delay to the clock input of FF1) + max(Clk-to-Q delay of FF1) +max(cell delay of inverter) + max(2 wire delay- "Qof FF1-to-inverter"and "inverter-to-D of FF2")
=Td = 2+11+9+(2+2) = 26ns
Clock path Delay
= (Clock period) + min(wire delay from CLK to Buffer input) + min(cell delay of Buffer) + min(wire delay from Buffer output to FF2/CLK pin) -(Setup time of FF2)
=Tclk = 15+2+5+2-4=20ns
Setup Slack = Tclk - Td = 20ns - 26ns = -6ns.
Since Setup Slack is negative -> Setup violation.
If Clock period is 22ns then
Tclk = 22+2+5+2-4=31-4=27ns AND Td = 26ns
Setup Slack = Tclk - Td = 27-26=1ns (No Violation)
Notes: http://www.vlsi-expert.com/2011/05/example-of-setup-and-hold-time-static.html

## Slide 17
Hold Analysis
Minimum Delay along the data path.
Maximum Delay along the clock path.
Delay in Data path
= min(wire delay to the clock input of FF1) + min(Clk-to-Q delay of FF1) +min(cell delay of inverter) + min(2 wire delay- "Qof FF1-to-inverter" and"inverter-to-D of FF2")
=Td = 1+9+6+(1+1)=18ns
Clock path Delay
= max(wire delay from CLK to Buffer input) + max(cell delay of Buffer) + max(wire delay from Buffer output to FF2/CLK pin) + (hold time of FF2)
=Tclk = 3+9+3+2 = 17 ns
Hold Slack = Td - Tclk = 18ns -17ns = 1ns
Since Hold Slack is positive-> No hold Violation.
Note:
If the hold time had been 4 ns instead of 2 ns, then there would have been a hold violation.
Td=18ns and Tclk = 3+9+3+4=19ns
So Hold Slack=Td - Tclk = 18ns - 19ns = -1ns (Violation)

## Slide 18: Summary
Delays in digital systems
  Propagation delay
  Contamination delay
Flip-flop timing constraints
  Setup time (ts)
  Hold time (th)
Cycle time determined by maximum delay
Correct operation depends on minimum delay
Clock skew affects both

## Slide 19: How to read your timing report

## Slide 20: How to Read and Interpret Timing Report

## Slide 21: Constraint File (note. These numbers may not match the following slides)
//設定clock, I/O 限制
create_clock "clk" -name clk -period 2 -waveform {0 1.7}
set_clock_uncertainty 0.2 clk
set_fix_hold all_clocks()
set_input_delay 0.5 -clock clk {in}
set_output_delay -max 0.8 -clock clk {isprime}
//設定 loading
set_load -pin_load 5 {isprime}
//Note: these commands are for practical applications to include
// clock jitter, input/output loading capacitances

## Slide 22: (Optional)

## Slide 24: Clock Network and Clock Skew

## Slide 25: Specify Timing Assertions (Optional)

## Slide 26: Timing Verification of Synchronous Designs

## Slide 27
Clock skew
Notes: Static Timing Verification of FF2: Setup

## Slide 29: Four Sections in a Timing Report

## Slide 30: Data Arrival Section

## Slide 31: Data Required Section

## Slide 32: Summary - Slack