## Slide 1: Lecture 6 Arithmetic
Tian Sheuan Chang

## Slide 2: Signed and unsigned Addition and multiplication

## Slide 3: Negative Integers
Thus far we have only addressed positive integers. What about negative numbers?
3 ways to represent negative integers in binary:
  Sign Magnitude
  One’s complement
  Two’s complement
Example: Consider +23 –23
  Sign Magnitude 0 10111 1 10111
  One’s complement 0 10111 1 01000
  Two’s complement 0 10111 1 01001
Sign bit

## Slide 4: Why do we all use 2’s complement?
2’s complement makes subtraction easy
Represent negative number, –x as 2n – x
All arithmetic is done modulo 2n so no adjustments are necessary
  x + (– y) = x + (2n – y) (mod 2n)
  consider 4-bit numbers
  4 – 3 = 4 + (16 – 3) (mod 16) = 4 + (15 – 3 + 1) = 0100 + (1111 – 0011) + 0001 = 0100 + 1100 + 0001 = 0001
Notes: 舉例說明 -7 = 8-7 =1 = 001 + sign bit = 1001
2’s complement 0111 => 1001
16-3 = 15-3 + 1 (2’s complement form)

## Slide 5: Signed data types (after Verilog-2001)
Type casting
  A = $signed(B) //sign extension of sign bit
  A = $unsigned(B) //zero fill B and assign it to A
Signed Based Values
  3’sh2 //3-bit signed hex value
  -3’sh4 //3-bit signed hex value
  A decimal number is always signed
2’s complement
logic signed [5:0] a;
logic [2:0] b;
b = 3’b101;
a = $signed(101); //a = 111_101;
a= $unsigned(101); //a = 000_101;
Notes: 舉例 sign extension -3 (5-bit) a(6bit) = $signed(101)
A = $unsigned(B) will zero fill B and assign it to A. Casting using $signed(signal_name) will sign extend the input. For example, A = $signed(B). If the sign bit is X or Z the value will be sign extended using X or Z, respectively. Assigning to a smaller bit width signal will simply truncate the necessary MSB’s as usual. Casting to the same bit width will have no effect other than to remove synthesis warnings.

## Slide 6: 無號數及有號數的乘加運算電路 (DIY Sign Extension in Verilog)
設計一個電路計算a * b + c，
  mode=0時，採用unsigned operation，
  mode=1時，採用signed operation

## Slide 7: Sign Extension in Verilog for Addition
module add_signed_1995 (
input [2:0] A,
input [2:0] B,
output [3:0] Sum
);
assign Sum = {A[2],A} + {B[2],B};
endmodule // add_signed_1995
module add_signed_2001 (
input signed [2:0] A,
input signed [2:0] B,
output signed [3:0] Sum
);
assign Sum = A + B;
endmodule // add_signed_2001
You have to deal with sign extension by yourself in Verilog 1995
Use signed for auto handling
module add_carry_signed_final (
input signed [2:0] A,
input signed [2:0] B,
input carry_in,
output signed [3:0] Sum
);
assign Sum = A + B + $signed({1'b0,carry_in});
endmodule // add_carry_signed_2001
Mixed signed/unsigned operation is regarded as unsigned
use $signed for type casting
http://www.tumbush.com/published_papers/Tumbush%20DVCon%2005.pdf
carry_in is unsigned, add “0” before type casting
Notes: http://www.tumbush.com/published_papers/Tumbush%20DVCon%2005.pdf

## Slide 8: Sign Extension in Verilog for Multiplication
module mult_signed_1995 (
input [2:0] a,
input [2:0] b,
output [5:0] prod
);
wire [5:0] prod_intermediate0;
wire [5:0] prod_intermediate1;
wire [5:0] prod_intermediate2;
wire [2:0] inv_add1;
assign prod_intermediate0 = b[0] ? {{3{a[2]}}, a} : 6'b0;
assign prod_intermediate1 = b[1] ? {{2{a[2]}}, a, 1'b0} : 6'b0;
// Do the invert and add1 of a.
assign inv_add1 = ~a + 1'b1;
assign prod_intermediate2 = b[2] ? {{1{inv_add1[2]}}, inv_add1, 2'b0} : 6'b0;
assign prod = prod_intermediate0 + prod_intermediate1 + prod_intermediate2;
endmodule
MSB is sign bit, appy 2’s complement
Notes: Intermediate product term: sign extension
Final MSB: 2’s complement

## Slide 9: Sign Extension in Verilog for Multiplication
module mult_signed_2001 (
input signed [2:0] a,
input signed [2:0] b,
output signed [5:0] prod
);
assign prod = a*b;
endmodule
module mult_signed_unsigned_2001 (
input signed [2:0] a,
input [2:0] b,
output signed [5:0] prod
);
assign prod = a*$signed({1'b0,b});
endmodule
b is unsigned, add “0” before type casting so as a positive number
Careful on mixed sign and unsigned operations

## Slide 10: Summary: Sign Extension in Verilog
http://www.sutherland-hdl.com/papers/2006-SNUG-Boston_standard_gotchas_presentation.pdf
Math operations are context-determined
  Signed arithmetic is done if all operands are signed
  But,… If any operand in the context is unsigned, then unsigned
To avoid this Gotcha…
  Engineers must know Verilog’s context-operation rules!
sum = a + b + signed’({1’b0,ci});
arithmetic is done
logic signed [3:0] a, b;
logic ci;
logic signed [4:0] sum;
sum = a + b + ci;
Unsigned adder, even though a, b and sum are signed
Unsigned adder, even though a, b and sum are signed
Size context is largest vector on left and right sides
  a, b and ci are extended to 5 bits before being added
Sign context is only the operands on right side
  ci is unsigned, so the context is unsigned
  a and b are converted to unsigned and zero extended
Gotcha!
Signed adder that subtracts carry in
signed
sum;
sum =
Signed adder that subtracts carry in
a, b and ci are signed, so the context is signed
if ci is 1, sign extending to 5 bits gives 11111 (binary)
  As a signed value, 11111 (binary) is -1!
logic
signed
[3:0] a, b;
ci;
logic logic
signed signed [4:0]
a + b + ci;
Gotcha!
Gotcha!
Gotcha!
Notes: http://www.sutherland-hdl.com/papers/2006-SNUG-Boston_standard_gotchas_presentation.pdf

## Slide 11: Summary
Beware of the signed arithmetic
  Cast $sign for unsigned operator
  Use sign declaration
  Let the Verilog tools do the rest

## Slide 12: 實際乘法怎麼做
簡單結論
  assign a = b * c; //注意所需輸出a 精確度 m-bit * n-bit = (m+n) bit
那不同加法架構做法呢?
  交給synthesis tool根據面積速度功耗限制 自動決定
那我可以知道tool到底幫我選了何種架構嗎?
  Design compiler: report_resources

## Slide 13: Bitwidth Problem
Rule
  During the evaluation of an expression, interim results shall take the size of the largest operand (in case of an assignment, this also includes the left-hand side)
Notes: https://www.eg.bucknell.edu/~csci320/2016-fall/wp-content/uploads/2015/08/verilog-std-1364-2005.pdf

## Slide 14
logic [15:0] a, b, answer; // 16-bit regs
assign answer = (a + b) >> 1; //will not work properly
//中間值計算只用16bit, carry bit 會在 做 >>1 前 就被忽略
assign answer = (a + b + 0) >> 1; //will work correctly
//better way
logic [16:0] answer_w;
assign answer_w = (a + b) >> 1; //wider bitwidth declaration
////////////////////////////////////////////
//assume only needs top 4-bits results
logic [3:0] c, d, answer_msb;
logic [7:0] tmp_w;
assign answer_msb = a * b; //only the lower 4bits remained, error
assign tmp_w = a * b;
assign answer_msb = tmp_w[7:4]; //correct

## Slide 15: Overflow (Optional)
Normal Condition (沒有Overflow)
  (+6) + (-3) = (+3)
故意使用4 bit的+6與3 bit的-3相加，若直接將兩個signed值相加，答案為-7
因為4 bit與3 bit相加，結果可能進位到5 bit，正確的作法是將4 bit的+6做signed extension到5 bit，且3 bit的-3也要做signed extension到5 bit後，然後才相加，若最後進位到6 bit，則不考慮6 bit的值‧

## Slide 16
Boundary Condition (正Overflow)
  (+7) + (+3) = (+10)
故意使用4 bit的+7與3 bit的+3相加，若直接將兩個signed值相加，答案為-6
+7與+3必須做signed extension才能相加，這樣才能得到正確答案+10‧
+10必須動到5 bit才能顯示，若輸出的值域為4 bit，只能-8 ~ +7，+10很顯然已經正overflow了
若只能以4 bit表示，因為是正的，MSB必須是0(SUM[3]=0)，所以若MSB是1就表示由進位而來，也就是正overflow了(此例的SUM[3]為1，所以已經正overflow)，再加上因為目前運算結果為5 bit，且是正，所以SUM[5]必須為0。
也就是說，若SUM[5]=0且SUM[4]=1時，為正overflow，所以01010對於4 bit來說，是正overflow。
Notes: 若只能以4 bit表示，因為是正的，MSB必須是0(SUM[3]=0)，所以若MSB是1就表示由進位而來，也就是正overflow了(此例的SUM[3]為1，所以已經正overflow)，再加上因為目前運算結果為5 bit，且是正，所以SUM[5]必須為0。
也就是說，若SUM[5]=0且SUM[4]=1時，為正overflow，所以01010對於4 bit來說，是正overflow。

## Slide 17: Optional
Boundary Condition (負Overflow)
  (-5) + (-4) = (-9)
故意使用4 bit的-5與3 bit的-4相加，若直接將兩個signed值相加，答案為-1
-5與-4一樣必須做signed extension才能相加，這樣才能得到正確答案-9‧進位到6 bit的1要捨去
-9必須動到5 bit才能顯示，若輸出的值域是4 bit，只能-8 ~ +7，-9很顯然已經是負overflow了‧
若只能以4 bit表示，因為是負的，MSB必須是1(SUM[3]=1)，所以若MSB是0就表示由進位而來，也就是負overflow了(此例的SUM[3]為0，所以已經負overflow)，再加上因為目前運算結果為5 bit，且是負，所以SUM[5]必須為1‧
也就是說，若SUM[5]為1且SUM[4]為0時，為負overflow，所以10111對於4 bit來說，是負overflow

## Slide 18
m bit + m bit => (m+1) bit
m bit + n bit => (m+1) bit，其中n < m
  m bit與n bit都必須先做signed extension到(m+1) bit才能相加
  若結果有到(m+2) bit則忽略之，實際的結果為(m+1) bit
若Sum[m+1] ^ Sum[m]為1，表示有overflow
  若Sum[m+1]為0且Sum[m]為1，則為正overflow
  若Sum[m+1]為1且Sum[m]為0，則為負overflow